## Slide 1: WF on Rel-16 NR HST PUSCH BS demodulation requirements
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, 20 – 30 Apr., 2020
Agenda: 6.17.2.2
R4-2005534
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
Agreed WFs for PUSCH in previous meetings
  R4-1910128 Way forward on NR HST BS demodulation requirements, RAN4#92.
  R4-1912809 Way forward on NR HST PUSCH demodulation requirements, RAN4#92Bis.
  R4-1915886 Way forward on NR HST PUSCH demodulation requirements, RAN4#93.
Agreed WFs for PRACH in previous meetings
  R4-1910128 WF on NR BS HST demodulation requirements , RAN4#92.
  R4-1912729 WF on NR HST BS PRACH demodulation requirements, RAN4#92b.
  R4-1915871 Way forward on NR HST PRACH demodulation requirement, RAN4#93.
Agreed WFs for BS demod in previous meetings
  R4-2002405, WF on Rel-16 NR HST BS demodulation requirements, RAN4#94-e. (The content in WF R4-2002405 except slide 16 is agreed; see meeting minutes.)
Corresponding Email summary in RAN4#94-e-Bis
  R4-2005594 Email discussion summary for [94e Bis][223] NR_HST_Demod_BS.

## Slide 3: Specification text
Agreements from 1st round
  Organisation of high-speed train requirement sections for PUSCH 500kph in specifications
    Re-use the HST PUSCH section currently used for 350kph to capture 500kph requirements
  Formalization of “l0=2 or l0=3” notes in TS 38.104 specification
    Minimum performance requirement specification (TS 38.104) does not explicitly capture the “l0=2 or l0=3” option in its test parameter. The options are captured in the FRC descriptions.
  Renaming of HST scenario 1
    No change to HST scenario naming.

## Slide 4: Specification Text
Organisation of high-speed train requirement sections for PUSCH 500kph in specifications
  Agreement 2nd round (online session):
    One new table for 500kph requirements.

## Slide 5: Specification Text
Organisation of high-speed train requirement sections for PUSCH DFT-s-OFDM in specifications
  Option 1: In HST PUSCH section currently used for 350kph (e.g., 38.104 section 8.2.4)
    New test parameter table and minimum requirements tables(s) for “transform precoding = on”.
  Option 2: TBD after DFT-s-OFDM agreement.
  Proposed WF
    TBD after DFT-s-OFDM introduction agreement.

## Slide 6: Specification Text
Organisation of high-speed train requirement sections for PUSCH fading channel under high Doppler in specifications
  Option 1: Introduce in non-HST PUSCH section.
  Option 2: Introduce in HST PUSCH section.
  Option 3: TBD after PUSCH fading channel under high Doppler agreement.
  Proposed WF
    TBD after PUSCH fading channel under high Doppler agreement.

## Slide 7: Applicability rules and declarations
Agreements from 1st round
  Relationship between TDD and FDD requirements
    Same requirements applicable for FDD and TDD; only one case simulated for result delivery. Parameter tables show SRS mapping for FDD and TDD separately.

## Slide 8: Applicability rules and declarations
High speed implicit test passing
  Agreement 2nd round (online session):
    Allow implicit test passing. A BS that declares to support 500kph, and passes the tests for 500kph, can also consider the tests for 350kph as passed.

## Slide 9: Applicability rules and declarations
High speed support declaration for HST PUSCH
  Option 1: Declare category of supported maximum speed. This can be either 350 or 500kph (or no HST support). Which tests need to be passed, if 500kph is declared, is discussed separately under “High speed implicit test passing”
  Option 2: Declare category of supported design target speed(s). This can be 350 or 500 or 350&500kph (or no HST support). Only the corresponding requirements are tested (only 350&500kph tests both).
  Proposed WF
    Companies are encouraged to bring specific manufacturer declaration proposals in a form that could be included in the manufacturer declaration table, i.e., all declaration groups, all choices per group, and explanation of each choice.

## Slide 10: Applicability rules and declarations
If Dft-s-OFDM is introduced: Applicability rule
  Option 1: Similar applicability rule for waveforms as existing PUSCH performance requirements will be used for HST
  Option 2: TBD after DFT-s-OFDM decision.
  Proposed WF
    TBD after DFT-s-OFDM introduction agreement.

## Slide 11: Configurations to be tested
Agreements from 1st round
  If 1T1R requirement is introduced: 1T1R requirement configuration
    Re-use the 1T2R requirement configuration.
  Slot allocation
    Only capture to use TDD pattern according to the previous WF agreement [R4-1915886]: Reuse the existing TDD configurations. 15 kHz SCS: 3D1S1U, S=10D:2G:2U 30 kHz SCS: 7D1S2U, S=6D:4G:4U

## Slide 12: Configurations to be tested
Introduce 1T1R requirements for the tunnel scenario
  Previous applicability rule wording options (Informative):
  Option 3 : Define test applicability rule in the section 8.1.2.0 of TS 38.141-1 as:
    Unless otherwise stated, for a BS supporting different numbers of antenna connectors (for BS type 1-C) or TAB connectors (for BS type 1-H) (see D.37 in table 4.6-1), the tests with low MIMO correlation level shall apply only for the lowest and highest numbers of supported connectors, and the specific connectors used for testing are based on manufacturer declaration.
  Option 4: Define test applicability rule in the section 8.1.2.0 of TS 38.141-1 as:
    “In high speed train requirements, unless otherwise stated, for a BS supporting different numbers of antenna connectors (for BS type 1-C) or TAB connectors (for BS type 1-H) (see D.37 in table 4.6-1), the tests with low MIMO correlation level shall apply only for the lowest number or two supported connectors, in addition to the highest numbers of supported connectors, and the specific connectors used for testing are based on manufacturer declaration.”
  Agreement 2nd round (online session)
    RAN4 will introduce 1T1R for the tunnel scenario requirements only for conducted requirements, FFS for the test applicability rule

## Slide 13: Configurations to be tested
If 1T1R requirement is introduced: MCS configuration
  Option 1: If 1T1R requirement is introduced, only have MCS 2 requirements.
  Option 2: If 1T1R requirement is introduced, have MCS 2 and MCS16 requirements.
  Proposed WF:
    TBD after 1T1R introduction agreed.
If 1T1R requirement is introduced with OTA testing: 1T1R requirement configuration
  Agreement 2nd round:
    Do not introduce OTA testing.

## Slide 14: Configurations to be tested
Dft-s-OFDM waveform
  Option 1: Introduce PUSCH HST requirements for DFT-s-OFDM.
  Option 2: Do not introduce PUSCH HST requirements for DFT-s-OFDM
  Option 3: Define DFT-s-OFDM only for 350km/h scenario, 1T2R and minimum channel bandwidth
  Proposed WF:
    Discuss in next meeting. Clarify how/if implicit test passing is still applicable.
If Dft-s-OFDM is introduced: Configuration
  Option 1 Configuration as follows. 500kph only, MCS2, RB allocation: 24 RB for 5MHz CBW/15KHz SCS, TDRA: type A, DMRS position: 1+1+1, L0: 3.
  Option 2: Minimum channel bandwidth (i.e., 5MHz for 15 kHz SCS, 10MHz for 30 kHz SCS)
  Option 3: Define HST requirements with DFT-s-OFDM for both 350 km/h and 500 km/h.
  Option 4: TBD after Dft-s-OFDM decision.
  Proposed WF:
    TBD after DFT-s-OFDM introduction agreement.

## Slide 15: Configurations to be tested
Multi-path fading channel under high Doppler value
  Option 1: Do not specify requirements for multi-path fading channel models with high Doppler values.
  Option 2: Specify PUSCH requirements for multi-path fading channel with maximum doppler shift of 1200Hz and 2400Hz for 15kHz SCS and 30kHz SCS, respectively.
  Option 3: Specify PUSCH requirements for multi-path fading channel with maximum doppler shift of 600Hz and 1200Hz for 15kHz SCS and 30kHz SCS, respectively.
  Proposed WF:
    FFS until next meeting.
Is multi-path fading channel under high Doppler value a common scenario?
  Option 1: Multi-path fading channel is very rare in HST scenarios (open area or tunnel).
  Option 2: Fading channel is also typical condition in the real propagation under high speed.
  Proposed WF:
    FFS until next meeting.

## Slide 16: Configurations to be tested
Additional CBW and SCS combinations
  Agreement 2nd round:
    Keep previous agreement.
    Add requirements for 5MHz CBW/15kHz SCS, 10Mhz CBW/30kHz SCS for CP-OFDM with applicability rule as for Rel-15 (i.e., only largest CBW per SCS needs to be tested).

## Slide 17
Simulation assumption for PUSCH (Informative)
Parameter | Value |  |  |  | 
 | v = 350km/h |  | v = 500km/h |  | 
Transform precoding | Disabled FFS: Enabled |  | Disabled FFS: Enabled |  | 
Number of Tx | 1 |  | 1 |  | 
Number of Rx | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | 
Number of layers | 1 |  | 1 |  | 
SCS | 15kHz, 30kHz |  | 15kHz, 30kHz |  | 
Reference signal | DMRS type 1 with 1+1+1 |  | DMRS type 1 with 1+1+1 |  | 
l0 | l0 = 2 or 3 |  | l0 = 2 or 3 |  | 
symbols length | 14 |  | 14 |  | 
start symbol index | 0 |  | 0 |  | 
Time domain resource allocation type | type A |  | type A |  | 
Frequency domain resource | Full applicable test bandwidth |  | Full applicable test bandwidth |  | 
MCS index | Tunnel: MCS 2 and MCS 16 Open space: MCS 2 and MCS 16 MCS2 and [16] for 1T1R |  | Tunnel: MCS 2 and MCS 16 Open space: MCS 2 and MCS 16 MCS2 and [16] for 1T1R |  | 
Maximum Doppler shift | 15kHz SCS: 1340Hz | 30kHz SCS: 2334Hz | 15kHz SCS: 1740Hz |  | 30kHz SCS: 3334Hz
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz |  | 15kHz SCS: 1.8GHz (Band n3) 30kHz SCS: 3.6GHz |  | 
Propagation condition | HST single-tap channel model: Tunnel: Ds=300m, Dmin=2m Open space: Ds=700m, Dmin=150m FFS: Multi-path fading channel under high Doppler value 15kHz: [1200]/[600]Hz; 30kHz: [2400]/[1200]Hz |  |  |  | 
SCS and BW | 15kHz: 10MHz/5MHz; 30kHz: 40MHz/10MHz |  |  |  | 
Number of HARQ transmissions | 4 |  |  | 4 | 
Testing metric | SNR @70% of maximum throughput |  |  | SNR @70% of maximum throughput |