## Slide 1: Way forward on CA CQI reporting requirements
China Telecom
3GPP TSG-RAN4 Meeting #94e-Bis
Electronic Meeting, 20 – 30 Apr., 2020
Agenda item: 6.18.1.5
R4-2005548
Document for: Approval

## Slide 2: Test Parameters
Duplex mode and SCS
  Option 1: Reuse the combinations and applicability rules from PDSCH CA Option 2:
    FR1: FDD + FDD with 15 kHz SCS and TDD + TDD with 30 kHz SCS
    FR2: TDD + TDD with 120 kHz SCS
    Channel Bandwidth
  Define performance requirements for all channel bandwidths listed in TS 38.101-1 and TS 38.101-2 for FR1 and FR2.
  Further discuss the test applicability rule
Propagation condition
  AWGN

## Slide 3: Test Parameters cont’d
  TDD pattern
  For 15kHZ SCS, if agreed to cover TDD 15kHz
    Option 1: 3D1S1U with S=10:2:2
  For 30kHz SCS: 7D1S2U with S=6:4:4
  For 120kHz SCS
    Option 1: 3D1S1U with S=10:2:2
    Option 2: 2D1S1U with S=11:3:0
    CSI reporting type
  Periodic CSI reporting
    CSI reporting periodicity
  5 slots for 15kHz SCS, 10 slots for 30kHz SCS
  for 120kHz SCS
    Option 1: 10 slots
    Option 2: 8 slots

## Slide 4: Test Parameters cont’d
CQI Table
  For FR1: CQI Table 2
  For FR2: CQI Table 1
Antenna configuration for CA CQI test
  Option 1: 1T2R and 1T4R
  Other options are not precluded
Signal power density for 2Rx and 4Rx bands
  Option 1: For 4Rx band, reduce the signal power density by 3dB compared to that for 2Rx
  Other options are not precluded

## Slide 5: Test Metric
General principle
  Option 1: Following the methodology used in LTE, measure the difference between the wideband CQI indices of Pcell and the first Scell as well as the difference between the wideband CQI indices of the first Scell and the other Scell(s) (if any).
  Other options are not precluded
  SNR configuration for 2DL CA CQI test
  Option 1: SNRPcell = 10dB and SNRScell = 4dB
  Other options are not precluded
  SNR configuration for 3 or more DL CA CQI test
  Option 1: SNRPcell = 12dB, SNRScell1 = 6dB, SNRScell2, 3,… = 0dB
  Other options are not precluded
    Delta CQI threshold for CA CQI test
  Option 1: thr = 2 for 2 or more DL CA
  Other options are not precluded