## Slide 1: WF on FR2 MIMO OTA
CAICT, Keysight, Spirent
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005556
Electronic Meeting, 20 – 30 Apr., 2020
Agenda item: 9.1.1
Document for: Approval

## Slide 2: FR2 MIMO OTA
FR2 PSP Validation procedures
  CE vendors align on the PSP validation procedure before next RAN4 e-meeting, e.g.,
    consider if Roll/AZ positioner could be used for SP method [R4-2005560]
    consider different virtual array configurations and NF compensation methods for the PAS estimation step for KS method [R4-2004565]
  If misalignment still shows next meeting, then better accuracy vs. measurement time will be the KPI to select one procedure to finalize this topic.
SNR analysis for 3D-MPAC
  Feasible SNR range shall be analyzed based on the agreed probe layout and channel model.
  The required SNR for FR2 CDL-A InO and CDL-C UMi shall be evaluated.
  Companies are encouraged to provide the input on simulation assumptions and simulation results.
  Select RMC based on the feasible SNR range and required SNR.

## Slide 3: FR2 MIMO OTA
FR2 3D-MPAC system layout
  6-probe locations in table below is agreed for FR2 3D-MPAC system layout
  Study potential ambiguities of relative positioning between probes, the 36 test points, the UE, and the channel model
  Study the blocking effect between positioner and NR MIMO probes
FR2 QoQZ procedure
  QoQZ procedure based on the agreed 6 probes location shall be finalized next RAN4 e-meeting