## Slide 1: WF on remaining issues for NR V2X system parameters
vivo, LGE...
3GPP TSG-RAN WG4#94-e-Bis Meeting R4-2005637
Electronic Meeting, 20 – 30 Apr., 2020

## Slide 2: Background
In this meeting, the progress for the following open issues is captured in this WF.
  1) The principles of introducing NR V2X licensed bands for SL operation
    The synchronization mechanism of Uu and SL in the TDD licensed bands
  2) The principles of introducing channel bandwidths for NR V2X licensed bands
    30MHz issue for NR V2X licensed band n38

## Slide 3: NR V2X band for SL operation
Proposal : NR band n79 for NR V2X SL operation with the conditions that the entire band is allocated for SL operation in a particular region or the SL operation is in sync with the non-V2X operation in the same band.
(Supported by CMCC, Huawei, vivo, CATT, OPPO)

## Slide 4: The sync mechanism of Uu and SL in the same TDD bands
Proposals (For clarification, Option 1~3 are bonded.)
  Option1: Divide NR V2X licensed TDD bands (partially used for SL) into two frequency spectrums: one used for Uu and the other used for SL.
  Option2: The division of this NR V2X licensed TDD bands is up to BS implementation or captured in the spec considering the requirements of Uu and SL traffic.
  Option3: For the synchronous operation between Uu and SL in the same licensed TDD bands, NR SL uses network as synchronization reference source.
  (supported by vivo, Huawei, Ericsson, CATT, Futurewei, VDF)
  Option4: In rel-16, only allow that the entire band is allocated for SL operation since the NR UL transmission will be impacted to the SL reception in the length of TA.
In the first round discussion, Option 3 was supported by the majority of companies.
In the second round, we can at least sort out the specific issues or impacts to the RF/RRM core requirements for the scenario NR licensed bands partially used for SL operation.

## Slide 5: The sync mechanism of Uu and SL in the same TDD bands (cont.’)
Companies can further discuss the RF architecture and the impacts on the core RF requirements for the following UE operations in the same TDD bands in the next meeting.
  NR UE operates in the licensed band through Uu interface only
  NR V2X UE operates in the licensed band through PC5 interface only
  NR V2X UE operates in the licensed band through Uu and PC5 synchronously

## Slide 6: Channel bandwidths for NR V2X licensed bands
Remove 30MHz for NR V2X licensed band n38 in TR 38.886.
Principle of introducing channel bandwidths for NR V2X licensed bands:
  Channel bandwidths defined for NR V2X licensed band should be a subset of UE channel bandwidths for the same licensed band in NR.
For Rel-16, channel bandwidths for NR V2X licensed bands should follow NR UE channel bandwidth definition.
If operators do have a request for introducing new channel bandwidths for NR V2X licensed bands, it can be treated in the enhanced sidelink WI for collecting operators’ request and define additional RF requirements related to these new channel bandwidths in Rel-17.

## Slide 7: References
[1] R4-2003024, NR V2X licensed frequency bands for SL operation, CMCC
[2] R4-2004744, On synchronization scenario for NR V2X in licensed band, Huawei, HiSilicon
[3] R4-2003676, Discussion on sync mechanism between SL and Uu in NR V2X licensed TDD bands, vivo
[4] R4-2003675, Further discussion on channel bandwidth for NR V2X licensed bands, vivo