## Slide 1: WF on con-current operation scenario and clarification
Dish Network,
3GPP TSG-RAN WG4 Meeting #94bis-e
Electronic Meeting, April 20 – 30 2020
R4-2005641

## Slide 2: Background (1/2)
Relevant aspects from RAN4#94e WF (R4-2002787):
Create generic requirements for these cases in Rel16 timeframe (by June 2020)
  NR Uu + NR SL (1st priority)
  LTE Uu + NR SL (1st priority)
  NR Uu + LTE SL (2nd priority, depend on RAN1/RAN2 specification progress)
  LTE/NR Uu + LTE SL + NR SL (2nd priority, depend on RAN1/RAN2 specification progress and discussion on slide 5)
    LTE SL and NR SL on same unlicensed band
Create requirements for band specific combinations based on operator requests
  For Rel-16, such operator requests shall only be considered for Uu and SL in different operating bands
    Vodafone:
      LTE Uu (B20) + NR SL (n38) in RAN4 #94e-Meeting
    DISH :
      NR Uu (n71) + NR SL (n47) in R4-1913968
      NR Uu (n71) + LTE SL (B47) in R4-1913968
      NR Uu (n71) + NR SL(n47) + LTE SL (B47) in R4-1913968 (In Rel-16 only if generic requirements are defined)
  It is possible to include band combination specific requirements when the respective generic requirements are ready within Rel-16 timeframe
  FFS: Whether the meaning “concurrent operation” should be further clarified in specifications

## Slide 3: Background (2/2)
First round summary (R4-2005096):
Issue 1-1: Con-current operation scenarios considered in Rel-16
Tentative agreements:
  One band combination is selected for each 2nd priority cases in Rel-16.
  For scenario of NR Uu + NR SL + LTE SL, n71 (NR Uu) + n47 (NR SL) +B47 (LTE SL) is considered, and the NR SL and LTE SL operate with TDM mode in the ITS band.
Issue 1-2: Clarification of con-current operation
Tentative agreements:
  Clarification of con-current operation is need, and the definition of con-current operation for V2X should be reflected in the TS.
  Con-current rather than concurrent should be used in the spec to align with the term used for LTE V2X.
Candidate options:
  Option 1: only the band combination where the Uu schedules/configures SL by semi-persistent way can be specified as concurrent operation
  Other options are not excluded. Companies are encouraged to provide options for con-current operation.

## Slide 4: WF
Issue 1-1: Con-current operation scenarios considered in Rel-16
  Band combinations for each 1st priority cases are specified in Rel-16
    n71 (NR Uu) + n47 (NR SL)
    B20 (LTE Uu) + n38 (NR SL)
  Band combinations for each 2nd priority cases will be specified in Rel-16
    For scenario of NR Uu + LTE SL, n71 (NR Uu) + B47 (LTE SL) is specified in Rel-16
    For scenario of NR Uu + NR SL + LTE SL, n71 (NR Uu) + n47 (NR SL) +B47 (LTE SL) is specified in Rel-16
      NR SL and LTE SL operate with TDM mode in the ITS band
Issue 1-2: Clarification of con-current operation
  Clarification of con-current operation is needed, and the definition of con-current operation for V2X shall be reflected in the TS
  Con-current rather than concurrent shall be used in the spec to align with the term used for LTE V2X
  Candidate options for con-current operation definitions:
    Option 1: only the band combination where the Uu schedules/configures SL by semi-persistent way can be specified as concurrent operation
    Option 2: the band combination where the Uu schedules/configures SL can be specified as concurrent operation
    Option 3: the band combinations where the Uu schedules/configures SL can be specified and which is agnostic as to the actual service being delivered on Uu and Sidelink interfaces
    Option 4: The simultaneous transmission and reception of sidelink and Uu interfaces where operation is agnostic of the service used on each interface.
    Other options are not excluded. Companies are encouraged to provide options for con-current operation