## Slide 1: Way forward on RF requirements for Tx switching between two uplink carriers
3GPP TSG-RAN WG4 Meeting #94e-bis
Electronic Meeting, 20 - 30 Apr., 2020
Agenda: 6.13.1.5
R4-2005664
China Telecom

## Slide 2: Background
Approved WFs in the previous meetings
  R4-1913041, RAN4 #92bis
  R4-1916084, RAN4 #93
  R4-2002815, RAN4 #94e

## Slide 3: Background on Applicability of DL interruption
  RAN4 #94e Agreement (Feb 2020):
For the following duplex mode combinations, no DL reception interruption (carrier 1 + carrier 2):
  SUL+TDD
  TDD+TDD CA with the same UL-DL pattern
  TDD+TDD EN-DC with the same UL-DL pattern
  For other duplex mode combinations, define different capabilities for UEs with and without DL interruption depending on the RAN1 feedback.
  …..
  Send LS to RAN1 and ask RAN1’s feedback on RAN1 spec impact if there is DL reception interruption in some scenarios.
  RAN1 #100bis-e (Apr 2020):
  RAN1 approved the reply LS to RAN4 in R1-2002960:
  RAN1 Answer: For UL Tx switching, there is no RAN1 specification impact on DL interruption. There may or may not be performance impacts due to DL interruption, but RAN1 did not analyze these further.
Notes:   RAN1 endorsed the following RAN1 Answer to RAN4:
  RAN1 endorsed the following RAN1 Answer to RAN4:

## Slide 4: Background on Applicability of DL interruption
  RAN4 94e-bis (Apr 2020):
  For duplex mode combinations excepting SUL+TDD and TDD+TDD with the same UL-DL pattern, RAN4 further discussed whether to introduce UE capability on DL interruption.
  According to the 1st round email discussion summary in R4-2005101, companies’ positions are as follows:
  Option 1: Define different capabilities for UEs with and without DL interruption (CMCC, ZTE, OPPO, Huawei, China Telecom, CHTTL, Apple MediaTek, vivo, CATT, Qualcomm)
    Option 1a: Whether to allow DL interruption for each band combination can be discussed later after the signaling for DL interruption is defined. (CMCC, Huawei, China Telecom, CHTTL, Apple, MediaTek, CATT, Qualcomm)
  Option 2: In Rel-16, only enable this feature for the band combinations that can avoid DL interruption, i.e., no interruption in DL reception are allowed. (Nokia, MediaTek, CATT)
    Option 2a (MediaTek, CATT)
      Introduce a band combination table or add a column in the CA/EN-DC table to indicate the support of this feature for each band combination. The WI can be closed if there is at least one combination is included.
    Option 2b (MediaTek, CATT)
      Introduce the below criteria of no DL interruption. Band combinations violate the criteria does not need to support switching capability.
        FGAP > 200MHz separation when TDD band <=2GHz.
        FGAP > 400MHz when 2GHz <=TDD band <=4GHz.
        FGAP > 800MHz when TDD band >=4GHz.

## Slide 5: WF (agreed)
Define different capabilities for UEs with and without DL interruption
  Whether to allow DL interruption for each band combination can be discussed later after the signaling for DL interruption is defined.
At the same time, RAN4 recognizes that DL interruption causes significant negative system impacts especially on LTE carriers in EN-DC scenarios [R4-2005101]
  Companies can provide more results in May

## Slide 6: DL interruption: interested band pairs from operators (for information)
Band pairs for FDD+TDD CA and FDD+TDD EN-DC (carrier 1 + carrier 2)
  Band (n)1 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)3 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)1 + Band n77 (KDDI)
  Band (n)3 + Band n77 (KDDI)
  Band (n)18 + Band n77 or n78 (KDDI)
  Band (n)28 + Band n77 or n78 (KDDI)
  Band (n)3 + Band n41 (CMCC)
  Band (n)3 + Band n79 (CMCC, docomo)
  Band (n)8 + Band n41 or n79 (CMCC)
  Band (n)8 + Band n77 or n78 (SoftBank)
  Band 11 + Band n77 or n78 (SoftBank)
  Band (n)5 + Band n78 or n79 (docomo)
  Band 19 + Band n78 or n79 (docomo)
  Band 21 + Band n78 or n79 (docomo)
  Band (n)1 + Band n79 (docomo)

## Slide 7
Thanks!