## Slide 1: WF on BS and UE IMT parameters for the SI on 6.425-7.125GHz and 10.0-10.5GHz
Agenda Item: 11.1
Document for: Approval
Source: CATT
3GPP TSG-RAN WG4 #94-e-Bis Tdoc R4-2005733
Electronic Meeting, 20 – 30 April, 2020

## Slide 2: Background
TSG RAN received the LS in [1] from ITU-R ,requesting parameters for IMT for sharing and compatibility studies.
TSG RAN initiated a study item for IMT parameters when operating above 6 GHz.
This WF concerns the LS reply for the following frequency ranges:
  6 425-7 025 MHz, 7 025-7 125 MHz and 10.0-10.5 GHz
9 discussion papers to RAN4#94-ebis were received.

## Slide 3: Agreements (1)
General parameters
  The IMT parameters provided to ITU-R should be chosen in a pragmatic way and be simple, non-ambiguous and easy to understand and implement in a study.
  IMT Parameters will be provided based on IMT licensed scenario.
  Duplex mode: TDD
  Channel bandwidth: 100MHz
    Due to co-existence with other systems, a smaller channel bandwidth could be used in 6.425-7.125GHz.
  Signal BW: SCS x NRB(SCS) x 12 for 100MHz CBW and 30kHz SCS
  SNR operating range: Reuse previous LS reply (RP-170021) or TR 38.803

## Slide 4: Agreements (2)
BS parameters for 6.425-7.125 GHz
  ACLR/ACS/SEM/Blocking: based on simulations
  Power dynamic range:
    Option 1: TS 38.104 clause 6.3.3 and 9.2.2
    Option 2: 0dB
  Spurious emissions:
    Option 1: TS 38.104 clause 6.6.5.2.1 and 9.7.5.2
    Option 2:
  30MHz ≤ f ≤ 1 GHz: -36dBm/100kHz
  1 GHz ≤ f ≤ Fbreak : -30dBm/1MHz
  Fbreak ≤ f ≤ 26 GHz: -20dBm/10MHz, with Fbreak is FFS.
  Maximum output power:
    Option 1: TS 38.104 clause 6.2 and 9.3
    Option 2: WA: [35, 45] dBm, MR and LA are FFS
  Average output power: N/A.
  Noise figure: Option 1: 7dB, Option 2: 5dB
  Reference sensitivity: Do not considered in the reply

## Slide 5: Agreements (3)
BS parameters for 10.0-10.5 GHz
  ACLR/ACS/SEM/Blocking: based on simulations
  Power dynamic range:
    Option1: TS 38.104 clause 6.3.3 and 9.2.2
    Option 2: 0dB
  Spurious emissions:
    Option 1: TS 38.104 clause 6.6.5.2.1 and 9.7.5.2
    Option 2:
  30MHz ≤ f ≤ 1 GHz: -36dBm/100kHz
  1 GHz ≤ f ≤ Fbreak : -30dBm/1MHz
  Fbreak ≤ f ≤ 26 GHz: -20dBm/10MHz, with Fbreak is FFS
  Maximum output power:
    Option1: TS 38.104 clause 6.2 and 9.3
    Option 2: FFS
  Average output power: N/A.
  Noise figure: 7dB
  Reference sensitivity: Do not considered in the reply

## Slide 6: Agreements (4)
UE parameters for 6.425-7.125 GHz
  ACLR/ACS/SEM: based on simulations
  Maximum output power: 23dBm, FFS on 20dBm
  Noise figure: 9dB
  Power dynamic range:
    Option 1: TS 38.101
    Option 2: 56dB
  Spurious emissions:
30MHz ≤ f ≤ 1 GHz: -36dBm/100kHz
1 GHz ≤ f ≤ 26 GHz: -30dBm/1MHz
  Average output power: N/A.
  Blocking:
    Option 1: 38.101
    Option 2: FFS
  Reference sensitivity: Do not considered in the reply

## Slide 7: Agreements (5)
UE parameters for 10.0-10.5 GHz
  ACLR/ACS/SEM: based on simulations
  Maximum output power: 23dBm, FFS on 20dBm
  Noise figure: 9dB
  Power dynamic range:
    Option 1: TS 38.101
    Option 2: 56dB
  Spurious emissions:
30MHz ≤ f ≤ 1 GHz: -36dBm/100kHz
1 GHz ≤ f ≤ 26 GHz: -30dBm/1MHz
  Average output power: N/A.
  Blocking:
    Option 1: 38.101
    Option 2: FFS
  Reference sensitivity: Do not considered in the reply

## Slide 8: References
R4-2003025, Discussion on IMT parameters for frequency ranges below 7.125GHz.
R4-2004129, SI on IMT parameters - Common parameters for 6.425-7.025GHz / 7.025-7.125 / 10.0 – 10.5 GHz, Ericsson.
R4-2004130, SI on IMT parameters - BS parameters for 6.425-7.025GHz / 7.025-7.125 / 10.0 – 10.5 GHz, Ericsson
R4-2004131, SI on IMT parameters - UE parameters for 6.425-7.025GHz / 7.025-7.125 / 10.0 – 10.5 GHz, Ericsson.
R4-2004144, Discussion on IMT parameters for 6.425-7.125GHz and 10-10.5GHz, ZTE.
R4-2004478, BS IMT technology related parameters for 6.425-7.025GHz and 7.025-7.125GHz, Huawei, HiSilicon.
R4-2004479, UE IMT technology related parameters for 6.425-7.025GHz and 7.025-7.125GHz, Huawei, HiSilicon.
R4-2004480, BS IMT technology related parameters for 10.0-10.5GHz, Huawei, HiSilicon
R4-2004481, UE IMT technology related parameters for 10.0-10.5GHz, Huawei, HiSilicon