## Slide 1: WF on MPE enhancements
OPPO
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005734 Electronic Meeting, 20 – 30 Apr., 2020

## Slide 2: PMPR reporting: values
Seven options have been provided in this meeting and merged into two options after 1st round. Further down selection is discussed in 2nd round.
  Option 1: 5 bits (up to 32 values), example values {1, 2, 3, …, 30, 31}
  Option 2: 2 bits (4 values), example values {3 ≤ P-MPR < 6, 6 ≤ P-MPR < 9, 9 ≤ P-MPR < 12, P-MPR ≥ 12}
Compromise is encouraged between Option 1 (5 bits) and Option 2 (2 bits), i.e. 2 to 5 bits
It is agreed that PMPR reporting values will take PC1 into account if there is difference comparing to PC3. And use PC3 as the baseline for the MPE discussion.
2nd round status | Option1 | Option2 | Others
Supporting companies | 5 | 6 | 1

## Slide 3: PMPR reporting: triggered report
PMPR report trigger threshold has been discussed and further down selection of following two options is discussed in 2nd round.
  Option 1: P-MPR is higher than a configurable threshold
  Option 2: RAN4 don't need to define PMPR report triggering mechanism, reuse the mechanism specified in TS 38.321.
Agreements:
  Option 1, i.e. P-MPR is higher than a configurable threshold
  Additionally, Option 2 can be further discussed at next meeting.
2nd round status | Option1 | Option2 | Either Option1 or 2 | Both Option 1 and 2
Supporting companies | 5 | 1 | 4 | 2

## Slide 4: PMPR reporting: Periodic report
Regarding “Whether periodic reporting is needed”, no conclusion can be reached in 1st and 2nd round discussion. Both options are almost equally supported.
  Option 1: No, only event triggered reporting is enough
  Option 2: Yes both are needed
To make progress, following solution has been given but not agreeable.
  Event triggered reporting is baseline approach and periodical report is optional for UEs to support.
No conclusion can be reached, continue discuss in next meeting.
2nd round status | Option1 | Option2 | No strong preference
Supporting companies | 4 | 4 | 2

## Slide 5: PMPR reporting: report before or after it is applied
It is agreed PMPR report after or on the grant is up to UE implementation. And this agreement will not be specified in UE specification TS38.101-2.

## Slide 6: PMPR reporting: ask for UL scheduling over PUCCH or RACH to report P-MPR
It is agreed RAN4 will not continue discuss “Whether UE is allowed to ask for UL scheduling over PUCCH or RACH to report its P-MPR” before necessity of this issue is clarified or request from other group is received.

## Slide 7: Dynamic duty cycle
About whether to introduce dynamic duty cycle reporting, down selection of following two options has been discussed in 2nd round:
  Option A: No
  Option B: If P-MPR granularity is less than 4-bits (particularly for 1-10dB P-MPR), a dynamic duty cycle should be reported to reduce estimation uncertainty in the value.
Agreements :
  Option A, i.e. dynamic duty cycle will not be introduced in Rel-16
2nd round status | Option1 | Option2 | No strong preference
Supporting companies | 7 | 3 | 1

## Slide 8: Optional or mandatory
Issue 1-3-1: Whether PMPR reporting is mandatory for rel-16 UE?
  Option 1: yes, no capability will be defined
  Option 2: no, new capability is defined
  Option 3: Other?
Agreements :
  Option 2, i.e. PMPR reporting is Optional for rel-16 UE
Issue 1-3-2: Whether dynamic duty cycle reporting is mandatory for rel-16 UE?
  Option 1: yes, no capability will be defined
  Option 2: no, new capability is defined
  Option 3: Other?
Agreements :
  No need to discuss since the conclusion is that dynamic duty cycle will not be introduced in Rel-16.
2nd round status | Option1 | Option2 | Others
Supporting companies | 0 | 6 | 3

## Slide 9: Reference PCMAX
It is agreed reference PCMAX will not be introduced.

## Slide 10: UE behavior after the network change (reduction) of the scheduled UL duty cycle
It is agreed UE behavior when NW reduces the UL duty cycle scheduling will not be introduced in spec.