## Slide 1: WF on BC based on SSB
Huawei, HiSilicon, [ ]…
R4-2005735
3GPP TSG-RAN WG4 #94bis-e
April 20th – 30th, 2020
Electronic meeting

## Slide 2
WF1: Beam correspondence requirement based on SSB-only
Whether BC based on SSB-only requirement is feasible:
  Yes, but need an applicability rule to avoid minimize increase in test cases and test time compared with Rel-15
how to define the applicability rule for peak direction:
  A single beam peak direction shall be chosen for other UL tests based on Rel-15 vs Rel-16 test-skipping rule:
    If a UE declares support for one of the Rel-16 RS, it skips Rel-15 tests and does all UL tests requiring MOP condition, based on the Rel-16 RS it declares support for. if the UE supports both types of RS, just it does one UL representative test (e.g. min peak EIRP testing) using the second RS. If a UE declares support for both types of RS, it should be able to meet all requirements with either set of RS. So the choice of ‘first’ or primary set of RS should be left to RAN5 discretion FFS on the detail procedure
how much performance relaxation, ∆p, relative to the condition which assumes both SSB and CSI-RS are present
  Option 1: Is feasible with ∆p = 0 dB
  Option 2: Is feasible with 0 < ∆p ≤ 3 dB
Side condition for BC based on SSB-only
  SSB min SNR level=6dB
Side condition for Tracking CSI-RS(use for DMRS of PDCCH)
  min SNR level=6dB

## Slide 3
WF2: capability for BC based on SSB-only
New capability for BC based on SSB-only is introduced:
  Whether it is mandatory with capability or optional with capability will be discussed in feature list group
Relationship to the Rel-15 capability
  Rel-16 beam correspondence enhancements can be applicable to both Rel-15 beam correspondence types of UEs (bit-0 and bit-1)
    Further discuss on the details in the next RAN4 meeting

## Slide 4: WF 3: Test case applicability
Rel-15 BC test is declared automatically passed if a UE passes Rel-16 BC test using the same SSB configuration and SNR as in Rel-15
  Further discuss on the details in the next RAN4 meeting
FFS for test case simplification if performance degradation for SSB based BC can be agreed