## Slide 1: WF on inter-band DL CA
Qualcomm,
R4-2005736
3GPP TSG-RAN WG4 Meeting #94Bis-e
Online, , 20th - 30th April 2020

## Slide 2: Way Forward on capability for beam management
CBM = common beam management between the band pair
IBM = independent beam management between the band pairs
How to distinguish between CBM and IBM band pairs will be further discussed and decided in RAN4#95.
  Choose between two alternatives:
    A) per band pair capability to declare IBM or CBM
    B) IBM / CBM band pairs defined in specification.
Network does not assume CBM UE supports non-co-located deployment
  This doesn’t mean the network cannot configure CBM UE in non-co-located deployment
Network assumes IBM UE supports both co-located and non-co-located deployments.

## Slide 3: IBM band pair requirements
PSD difference between bands in Refsens i.e. peak EIS:
  Agree PSD difference is within a range[6.5 – 30] dB and RAN4 aims to agree one number in RAN4#95
PSD difference between bands in EIS spherical coverage:
  Agree a range[6.5 – 30] dB and target to agree one number in RAN4#95