## Slide 1: On activation delay requirements for multiple SCell activation
Apple, …
R4-2006193
3GPP TSG-RAN4 Meeting #95-e
Electronic Meeting, 25th May - 5th Jun 2020
Agenda item: 6.15.1.2
Document for: Approval

## Slide 2: Background: Types of SCell activation in R15 TS38.133
To-be-activated target SCell types | Activation delay requirement in R15 TS38.133
Type 1: FR1 known SCell with meas_cyc=160ms | TFirstSSB+ 5ms
Type 2: FR1 Known SCell with meas_cyc>160ms | TFirstSSB_MAX + Trs + 5ms
Type 3: FR1 Unknown SCell | TFirstSSB_MAX + TSMTC_MAX + 2*Trs + 5ms
Type 4: FR2 SCell with active serving cell(s) on same band and with configured SMTC | TFirstSSB+ 5ms
Type 5: FR2 SCell with active serving cell(s) on same band but without configured SMTC, and the RS (s) of SCell being activated is (are) QCL-TypeD with RS (s) of one active serving cell on that FR2 band | 3 ms
Type 6: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting | 3 ms + max(Tuncertainty_MAC +TFineTiming + 2ms, Tuncertainty_SP)
Type 7: FR2 known SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ)
Type 8: FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting | 6ms+TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs + TL1-RSRP, measure + TL1-RSRP, report + THARQ + max(Tuncertainty_MAC + TFineTiming + 2ms, Tuncertainty_SP).
Type 9: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | 3ms + TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs + TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}.

## Slide 3: Scenarios in this contribution
  Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC.
  Scenario 2: In NR-DC, two MAC PDUs on dual NR CGs are received for multiple SCell activation in two CGs
  only for per-FR MG capable UE

## Slide 4: Activation delay analysis for Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC
Whether the victim Scell activation delay is changed from single SCell activation case or not? |  | Being-Activated SCell (victim) type |  |  |  |  |  |  |  |  | 
 |  | 1 (FR1) | 2 (FR1) | 3 (FR1) | 4 (FR2) | 5(FR2) | 6(FR2) | 7(FR2) | 8(FR2) | 9(FR2) | 10(FR2)
Being-Activated SCell (aggressor) type | 1 (FR1) | No | No | No | No | No | No | No | No | No | No
 | 2 (FR1) | Yes for intra-band (AGC) No for inter-band | No | No | No | No | No | No | No | No | No
 | 3 (FR1) | Yes for intra-band (AGC) No for inter-band | Yes for intra-band (AGC) No for inter-band | Yes due to searcher limitation | No | No | No | No | No | Yes due to searcher limitation | Yes due to searcher limitation
 | 4 (FR2) | No | No | No | No | No | N/A | N/A | N/A | N/A | N/A
 | 5 (FR2) | No | No | No | No | No | N/A | N/A | N/A | N/A | N/A
 | 6 (FR2) | No | No | No | N/A | N/A | No | No | No | Yes, reduced due to known aggressor | Yes, reduced due to known aggressor
 | 7 (FR2) | No | No | No | N/A | N/A | No | No | No | Yes, reduced due to known aggressor | Yes, reduced due to known aggressor
 | 8 (FR2) | No | No | Yes due to searcher limitation | N/A | N/A | No | No | No | No | No
 | 9 (FR2) | No | No | Yes due to searcher limitation | N/A | N/A | No | No | No | No | No
Note: Detailed analysis can be found in Annex A.
Activation delay needs extension
Activation delay needs reduction

## Slide 5: Proposal 1: Activation delay requirement for “Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC” is proposed as in following table.
To-be-activated target SCell types | Proposed activation delay with multiple SCell activation
Type 1 | TFirstSSB_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell. TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB+ 5ms, for all other cases
Type 2 | TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB_MAX + Trs + 5ms, for all other cases
Type 3 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 8*Trs*N2 +Trs +5ms where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. If no any parallel to-be-activated SCell on FR2 band, N2 =0.
Type 4 | Same as single SCell activation (TFirstSSB+ 5ms)
Type 5 | Same as single SCell activation (3 ms )
Type 6 | Same as single SCell activation (3 ms + max(Tuncertainty_MAC +TFineTiming + 2ms, Tuncertainty_SP))
Type 7 | Same as single SCell activation (max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ))
Type 8 | 3 ms + max(Tuncertainty_MAC +TFineTiming + 2ms, Tuncertainty_SP), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell. Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time 6ms+TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs *N2+ Trs*N1+ TL1-RSRP, measure + TL1-RSRP, report + THARQ + max(Tuncertainty_MAC + TFineTiming + 2ms, Tuncertainty_SP), if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known Scell where N1 is the number of parallel to-be-activated SCell which is FR1 unknown N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.
Type 9 | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell . Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time 3ms + TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs*N2+Trs*N1+ TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.

## Slide 6: Activation delay analysis for Scenario 2: two MAC PDUs on dual NR CGs are received for multiple SCell activation in two CGs of NR-DC for per-FR MG capable UE
In NR-DC, two MAC PDUs on dual NR CGs are received for multiple SCell activation in two CGs, NR DC means UE already has FR1 PCell and FR2 PSCell, then only type 4 and type 5 to-be-activated SCell shall be considered for FR2 here.
Proposal 2: reuse same requirement as in sub-topic 1-10 scenario (from issue 1-10-1 to issue 1-10-5), and no unknown FR2 Scell shall be considered. (sub-topic 1-11 R4-2005293)
To-be-activated target SCell types | Proposed activation delay with multiple SCell activation
Type 1 | TFirstSSB_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell. TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB+ 5ms, for all other cases
Type 2 | TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB_MAX + Trs + 5ms, for all other cases
Type 3 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 8*Trs*N2 +Trs +5ms where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. If no any parallel to-be-activated SCell on FR2 band, N2 =0.
Type 4 | Same as single SCell activation (TFirstSSB+ 5ms)
Type 5 | Same as single SCell activation (3 ms )