## Slide 1: WF on remaining issues on MPR and AMPR for intra-band non-contiguous CA
Skyworks, Qualcomm, Huawei, HiSilicon, Nokia
R4-2008471
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: WF on non-contiguous UL CA architecture and capabilities
At least three bandwidth separation class (= maximum instantaneous BW support):
  ≤ 100MHz
  ≤ 200MHz
  > 200MHz
Baseline architecture for PC3 Rel16 uses two 23dBm transmit chains in order to cope with the large instantaneous transmit BW (up to 600MHz)
2TX chain is the default assumption
if UL MIMO is supported in single CC mode it is not supported in CA mode unless extra transmit paths are signalled through specific UL MIMO signaling
2TX chain signaling is needed to cover declaration of two DC location instead of one
1PA architecture is not precluded for BW separation class ≤ 200MHz in future releases

## Slide 3: Background on 2PA non-contiguous UL CA MPR
Companies have submitted inputs and discussion papers [2,3,4]
It was suggested that DC_41_n41 MPR_IM3 values could be used as a starting point but:
  To account for the change in Reference for MPR between ENDC and CA 3dB must be subtracted to the ENDC MA values.
  ENDC MPR was derived to support PC2 thus margin exists for PC3 (SEM is absolute)
  In CA, each CC may use CP-OFDM that results in higher PAPR than SC-FDMA+CP-OFDM
  ENDC looked at maximum BW separation of 200MHz where ULCA has to cover up to 600MHz
  ENDC also has two MPR_IM3:
    one for -13dBm/MHz (IMD3 falling into each CC outer adjacent region)
    one for -30dBm/MHz (IMD3 falling beyond each CC outer adjacent region)

## Slide 4: WF on non-contiguous UL CA MPR specification
Specify two set of MPR for intra-band non-contiguous UL CA, for 1PA architecture and 2PA architecture respectively
  2PA architecture MPR is taken as the baseline in Release 16
Specify two set of MPR_IM3 for -13dBm/MHz and -30dBm/MHz Structure (BW inflexion point and relative steps) of ENDC MPR may be reused with MA reduced by 3dB as a reference point
Same MPR for CP-OFDM+CP-OFDM and DFT-s-OFDM+DFT-s-OFDM cases
  MPR values may be different per BW separation class (and MPR offset may be sufficient):
  One MPR for ≤ 100MHz and ≤ 200MHz BW separation class
  One MPR for > 200MHz BW separation class

## Slide 5: Starting point for MPR evaluation
-13dBm/MHz case: IMD3 falling in outer adjacent regions of the allocated CCs
MPRCA_IM3 = 9 ; 0 ≤B<0.54
7 ; 0.54 ≤B<1.08
6 ; 1.08 ≤B<2.16
5.5 ; 2.16 ≤B<3.24
5 ; 3.24 ≤B<5.4
3 ; 5.4 ≤B
-30dBm/MHz case: IMD3 falling beyond outer adjacent regions of the allocated CCs
MPRCA_IM3 = 15; 0 ≤B<1.08
14.5; 1.08 ≤B<2.16
14; 2.16 ≤B<3.24
13; 3.24 ≤ B < 5.04
12; 5.04 ≤B< 10.08
11; 10.08 ≤B< 16.56
10.5; 16.56 ≤ B < 21.96
10; 21.96 ≤B
MPRCA_IM3 values below can be considered as a starting point for the structure or the requirement and possibly valid for ≤ 200MHz BW separation class

## Slide 6: Assumptions for MPR evaluation
Based on 2x23dBm PAs
Antenna isolation is 10dB
PA calibrated for 30dBc ACLR at 22dBm with 20MHz 100RB0 DFT-s-OFDM QPSK waveform
Since same MPR is targeted CP-OFDM is used in each carrier
Equal PSD and Equal back-off power split
Worst case back-off IMD3 at -13dBm/MHz and -30dBm/MHz for 1RB+1RB at 15kHz and 30kHz SCS
  1RB+1RB separation of ~100, 200, 600MHz to cover variation across BW separation classes
  Other allocations sizes are recommended but the MPR vs allocation BW behavior from ENDC MPR can also be reused

## Slide 7
References in this meeting
References on Bandwidth definitions
[1] R4-2008150 on FR1 UL non-contiguous CA UE capability, Huawei, HiSilicon
[2] R4-2008151 on FR1 UL non-contiguous CA MPR requirement Rel-16, Huawei, HiSilicon
[3] R4-2008208 Non-contiguous ULCA MPR and Requirements, Qualcomm Incorporated
[4] R4-2008039 [FR1 NR ULCA] Non-contiguous UL CA Architecture, Signaling and MPR evaluation, Skyworks Solutions Inc.