## Slide 1: 3GPP TSG-RAN4 Meeting #95-e Electronic Meeting May 25 – Jun 5 , 2020 Agenda item: 6.11.3
Huawei, HiSilicon
Way forward for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes(eMBB)
R4-2008813
Document for: Approval

## Slide 2: Background
Agreed WF in the previous meetings:
  R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4#94-e
  R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4#94-e
  R4-2005529 WF on PDSCH demodulation requirement and General aspects for NR eMIMO, RAN4#94-e-Bis

## Slide 3: Performance requirements for multi-panel/TRP in FR1

## Slide 4: General test set-up for PDSCH requirements
Reference for timing offset/frequency offset
  Option 1:
    Using TP which carry on SSB transmission with default TCI state #0 as the reference TP (TP1)
    Timing offset = time offset among TP2 and TP1
    Frequency offset = frequency offset among TP2 and TP1
  Other options not precluded
Baseline receiver assumption for FFT window timing
  Option 1: Assuming UE always fix FFT timing based on TCI state #0 (TP1) as baseline assumption to define RAN4 performance requirements
  Option 2: FFT timing based on TRP with the highest RSRP on sync signals + fixed timing shift
  Option 3: FFT timing based on nearest TRP
  Other options not precluded

## Slide 5: General test set-up for PDSCH requirements
Timing offset among multi-panel/TRP
  Timing offset values
    Option 1: , = [-0.5, 2]μs
    Option 2: , = 2μs
    Option 3: FFS on Introducing timing offset which scaled with SCS ∆t=2^(−μ) ∆t1, Candidate values for simulation purpose: {-1, -0.5, 1, 3}
  Values for requirements definition should be derived based on performance analysis and analysis on typical TO distributions. Final values should ensure that reasonable UE implementations can meet the requirements
Frequency offset among multi-panel/TRP
  200Hz for FR1 FDD 15kHz, 300Hz for FR1 TDD 30kHz

## Slide 6: General test set-up for PDSCH requirements
TRS/CSI-RS configuration
  Taking non-colliding TRS/CSI-RS in multi-TRP/panel as baseline assumption meanwhile interested companies are encouraged to bring more analysis and evaluation results for non-colliding and colliding cases.

## Slide 7: Multi-DCI based PDSCH requirements
Resource allocation
  Option 1: Only non-overlapping cases
  Option 2: Both non-overlapping and full-overlapping cases
CRS rate-matching
  Do not define performance requirements for multi-DCI based multi-TRP with UE rate-matching around configured CRS pattern.
PDCCH configuration
  K0 = 0, AL = 8

## Slide 8: Multi-DCI based PDSCH requirements
PDSCH configuration for each TRP
  PDSCH resource mapping type: Type A
  Resource allocation type: Type 1
  DM-RS configuration: Type 1 with single-symbol DM-RS: 1+1
  Antenna ports indexes: {1000,1001} and {1002,1003}, i.e. different CDM groups for two TRPs
  Starting symbol (S): 2
  Time duration (L): 12
  Frequency domain: half of the maximum bandwidth by indicating the start resource block , the allocated resource blocks

## Slide 9: Multi-DCI based PDSCH requirements
PDSCH configuration for each TRP
  Antenna configuration:
    Option1: Only 2T2R, 2T4R
    Option2: Both 2T2R, 2T4R and 4T2R, 4T4R
Number of test cases
  Option1: 3 test cases per duplex mode
    Test 2a Multi- DCI with frequency offset and Non-overlapping scheduling
    Test 2b Multi DCI with positive time offset and Non-overlapping scheduling
    Test 2c Multi DCI with negative time offset and overlapping scheduling
  Other options are not preclude

## Slide 10: Single-DCI based multi-TRP/Panel
Introduce PDSCH demodulation requirements for Single-DCI based SDM scheme with full-overlapping resource allocation
  Layer combination: 1+1 for both 2Rx and 4Rx
  Number of TCI state: Two TCI states configuration
  Number of test cases
    Option 1: 3 test cases per duplex mode
      Test 1a Single DCI with frequency offset and overlapping scheduling
      Test 1b Single DCI with positive time offset and overlapping scheduling
      Test 1c Single DCI with negative time offset and overlapping scheduling
    Other options are not preclude

## Slide 11: Performance requirements for multi-panel/TRP in FR2

## Slide 12: Performance requirements for multi-panel/TRP in FR2
Necessity of introducing test case(s) for multi-panel/TRP transmission schemes in FR2
  Option 1: No
  Option 2: Do not define FR2 requirements for simultaneous reception from multi-TRP/Panel (eMBB) and Study testability for FR2 single-DCI based multi-TRP schemes 3 and 4
  Option 3: Further discuss technical details and relevance of single wide Rx beam reception in FR2

## Slide 13: TCI state configuration for FR2
Option 1: Single Type D
Other options not precluded
TCI index | Information |  | FR2
TCI state #0 | Type 1 QCL information | SSB index | SSB #0
 |  | QCL Type | Type C
 | Type 2 QCL information | SSB index | SSB #0
 |  | QCL Type | Type D
TCI state #1 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type D
TCI state #2 | Type 1 QCL information | CSI-RS resource | CSI-RS resource 2 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type A
 | Type 2 QCL information | CSI-RS resource | CSI-RS resource 1 from ‘CSI-RS for tracking’ configuration
 |  | QCL Type | Type D