## Slide 1: Way forward for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC)
Intel Corporation
3GPP TSG-RAN WG4 Meeting #95e
Electronic, 25th May – 5th June, 2020 Agenda Item: 6.11.3
R4-2008814

## Slide 2: Background
      Agreed WFs for demodulation requirements for NR eMIMO WI in previous meetings
        R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4 #94-e
        R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4 #94-e
        R4-2005529 WF on PDSCH demodulation requirement and general aspects for NR eMIMO, RAN4 #94e-Bis

## Slide 3: Candidate Schemes
URLLC single-DCI based multi-TRP/panel transmission schemes (see Annex)
  SDM scheme (1a)
  Repetition schemes:
    FDM scheme A (2a)
    FDM scheme B (2b)
    TDM scheme A (3)
    Inter-slot TDM scheme (4)

## Slide 4: Necessity of PDSCH requirements (Summary of the views from the first round discussion)
      Whether already agreed requirements for multi-DCI based and single-DCI based multi-TRP transmission scheme and URLLC single-TRP requirements can cover single DCI based URLLC multi-TRP transmission schemes
        Option 1: Yes. FDM schemes can be verified by multi-DCI based and single-DCI based SDM multi-TRP transmission schemes. TDM schemes can be verified by single-DCI based SDM multi-TRP transmission scheme and URLLC single-TRP slot aggregation
        Option 2: No. Each scheme is a separate UE feature. Different resource allocation approach comparing to single-DCI based SDM multi-TRP transmission scheme. Different CDM group and TBS calculation assumptions comparing to multi-DCI based and single-DCI based SDM multi-TRP transmission schemes. Non-synchronized (with TO/FO) transmission comparing to single TRP URLLC slot aggregation scenario. Specific sub-features for some schemes as: CW combining, number of repetitions.
        Option 3: Cannot cover at least FDM scheme A.

## Slide 5: PDSCH requirements introduction
      Whether to define requirements for single DCI-based multi-TRP/Panel URLLC schemes
        Option 1: Not need to define
        Option 2a: Yes, for schemes 2a, 2b, 3 and 4
        Option 2b: Yes, only for one scheme from FDM schemes and one from TDM schemes
      Make decision on whether to introduce test cases in Q3 2020
      Interested companies are encouraged to provide simulation assumptions on the next meeting in order to have sufficient time for requirements definition if they will be agreed to introduce on the next meeting
      Further discuss test applicability rule (If requirements will be agreed to define)
        Option 1: FDM scheme is skipped if UE passes the multi-DCI based multi-TRP transmission and/or TDM scheme is skipped if UE passes URLLC slot aggregation requirements
        Other options are not precluded

## Slide 6: Test metric
      Test metric for requirements definition
        Option 1: 1 % BLER which is more suitable for URLLC service
        Option 2: 70 % @ max throughput

## Slide 7: Annex
URLLC transmission schemes
  Single-DCI based SDM scheme
    Single RV in a slot, common FDRA, common TDRA, two CDM groups
  Single-DCI based FDM repetition scheme A
    Single RV in a slot, ~equally divided PRGs across TRPs, common TDRA, single CDM group, single PTRS port
  Single-DCI based FDM repetition scheme B
    RV pair in a slot, ~equally divided PRGs across TRPs, common TDRA, single CDM group, single PTRS port
SDM
FDM A
FDM B

## Slide 8: Annex (cont’d)
URLLC transmission schemes
  Single-DCI based TDM repetition scheme A
    RV pair in a slot, same FDRA, same symbol length of each Tx occasion, single CDM group, limited TBS
  Single-DCI based inter-slot TDM repetition scheme
    Single RV in a slot, common SLIV, common FDRA, number of Tx occasions 2-16, single CDM group, limited TBS
TDM A
Inter-slot TDM (2 Tx occasions)