## Slide 1: NB IoT Maintenance for FCC Regulation
MediaTek, Qualcomm
3GPP TSG-RAN WG4 Meeting #95-e R4-2008980
Electronic Meeting, 25th to 29th May 2020

## Slide 2: Background
FCC regulation is such that the outer channels cannot be used for NB-IoT on some bands [2] [3].
UEs need signaling in FCC conformance test such that these channels are not tested (they would fail 100KHz OOB spec)
In the network such signaling may not be required as the BS may just not allocate those channels.

## Slide 3: Background: proposed solution and concerns
Proposed solution by UE vendors:
  Use NS_04 like for band 26 for US bands to restrict usage of outer channels in the spec, otherwise UEs are not able to pass the FCC conformance test
  Regarding NBC:
    If there’s no NS broadcasted or NS is not supported, UE would apply NS_01 as default NS e.g. NS_01. This applies for the UE which supports original NS_01 if it operates other than band 26.
Concerns from Networks vendors:
  NS is might not be needed in reality from Networks side
  Behavior of legacy UEs other than band 26 if NS-04 signaled in the network

## Slide 4: WF if agreeable
Investigate and confirm there is no backward compatibility with legacy devices when introducing NS_04 or new NS_05 on bands 2, 5, 12, 17, 25, 26, 66.
If no issue:
  Option 1: Modify existing NS_04 to add more bands,w reducing all bands by 100kHz on each side.
  Option 2: Add NS_05 with A-MPR table accordingly and allow NBC
  Other options are not precluded.

## Slide 5: Reference
[1] R4-1815344 NBIOT B26 GB operation
[2] R4-2005219 WF on NB-IoT band edge performance against FCC
[3] R4-2003987 NBIOT guard band operation for FCC regulation considerations
[4] R4-2007564_Exclude 100kHz for NBIOT to meet FCC band-edge requirements
[5] R4-2006446 36101 CR for NBIoT-rel-14-catF-r2