## Slide 1: WF on band definition and corresponding requirements in 6 GHz for Rel-16 NR-U
Qualcomm Incorporated, Nokia, AT&T, Charter Communications, Inc., LG Electronics, Verizon
R4-200xxxx
3GPP TSG-RAN WG4 #95-e
May 25th ‒ June 5th, 2020
Electronic Meeting

## Slide 2: Background
Scope of work
  NR-U WID in [2] states among the objectives for RAN4
    Specify new unlicensed band(s) for the 5 GHz and 6 GHz frequency ranges (see Note 1). The band(s) definition should include UL/DL operation.
    Note 1: The actual frequency range for specification can be further discussed based on regulatory updates in the US and Europe.
  Agreed Way Forward in R4-1910386 states
    Option 1: Band X AND Band Y
    Band X: 5925 – 6425 MHz, Band Y: 5925 – 7125 MHz
Regulatory
  FCC has adopted and published rules [1] for Band Y in the US: https://docs.fcc.gov/public/attachments/FCC-20-51A1.pdf
  European countries, China, and elsewhere have not finalized regulations yet for usage of 6 GHz band
Market demand
  See [1]
Observation → Scope of work is defined in the WID and approved at RAN plenary. RAN4 cannot change the scope of work.

## Slide 3: Addressing company concerns
Additional workload and its impact to completion of NR-U work item
  NR-U work item is scheduled to complete in June 2020 for Rel-16, but due to COVID-19 situation and the lost efficiency of e-meetings in the past quarter, it is expected that the work item will be granted a 1Q extension
  Much of the work for NR-U to date has been on general band-agnostic requirements that can readily apply to 5 GHz and 6 GHz bands
  Some band-specific requirements for 6 GHz would need to be completed
Global regulatory uncertainty
  While regulations are clear in the US, there is less certainty in other countries
  Some companies propose that 3GPP wait for more global certainty in regulations before defining the 6 GHz band → Defer to Rel-17 with release independence back to Rel-16.
  3GPP should be responsive to timely regional market needs while also maintaining a global footprint

## Slide 4: Candidate options
Rel-17 with release independence back to Rel-16
  Not in accordance with WID or agreed WF
  Does not address the market demand in timely fashion. Rel-17 specification will not be published until Mid 2021? In the meantime, other shared technology has already announced product availability for 6 GHz now!
Truncated band 5925 – 6425 MHz
  Is not consistent with FCC R&O. The FCC made the entire range available for unlicensed, not a subset of it.
  A smaller band does not help reduce the workload
Define a US only band in 6 GHz for Rel-16
  Define Band 5925 – 7125 MHz with a note indicating applicability to US only
    Approach is similar to Band n95 which has a note “This band is applicable in China only”
  In the future, the band could have its applicability extended to other countries as regulations become more clear

## Slide 5: Way Forward on Band Definition
Define a US only band in 6 GHz for Rel-16 (5925 – 7125 MHz)
  Rules are fully available from the FCC for the US
  Uncertainty of regulations in other countries should not prevent enablement of 3GPP technologies in 6 GHz for the US
    Global incompatibility did not prevent enabling Band n95 in China only
  There is significant market demand now for unlicensed services in 6 GHz band. 3GPP technologies will not be considered if specifications are not available.
  Does not preclude the possibility of future licensed or unlicensed bands covering all or a portion of the same spectrum once regulations are finalized in other countries

## Slide 6: WF on general requirements
General requirements such as ACS, blocking, in-band emissions, ALCR, SEM, general spurious emissions, MPR are either already agreed or in the process of being discussed
General requirements are band-agnostic and can apply to 6 GHz band directly

## Slide 7: WF on US 6 GHz band-specific requirements
Channel bandwidths
  Same as Band n46
Channel raster/sync raster
  Follow the same procedure as Band n46,
  Aligned to draft 802.11ax/Wi-Fi 6E channelization
UE power class
  In principle, both PC5 and PC3 can apply same as Band n46
  Max Tx power may have to be reduced to comply with FCC requirements (see next bullet)
NS signaling to meet FCC emission and PSD requirements
  NS_51: 24 dBm max output power, -1 dBm/MHz max PSD, -27 dBm/MHz spurious emissions
  NS_52: 30 dBm max output power, 17 dBm/MHz max PSD, -27 dBm/MHz spurious emissions
Refsens to be evaluated with Band n46 refsens as starting point.
A-MPR for NS_51 and NS_52 to be evaluated
Analysis of 3GPP UE requirements to meet FCC rules can be found in [4].

## Slide 8: WF on DC and CA
No band combinations with 6 GHz are included in the NR-U WID
  DC and CA combinations with 6 GHz are therefore not specified in Rel-16
  Combinations can be added based on operator request in Rel-17 with release independence back to Rel-16

## Slide 9: References
[1] Report and Order and Further Notice of Proposed Rulemaking, Unlicensed Use of the 6 GHz Band, https://docs.fcc.gov/public/attachments/FCC-20-51A1.pdf
[2] RP-192926, “Revised WID on NR-based Access to Unlicensed Spectrum,” Qualcomm Inc.
[3] R4-1910386, “WF on NR-U 6 GHz band plan,” Qualcomm Incorporated
[4] R4-2008123, “NR-U 6 GHz Bands n96 and n97,” Qualcomm Incorporated