## Slide 1: WF on NR-U MPR
MediaTek Inc.
3GPP TSG-RAN WG4 #95-e Meeting R4-2008436 Online, May 25th – June 5th, 2020

## Slide 2: Background
NR-U MPR requirements have been evaluated in this meeting for both PC5 and PC3 (PC5 + PC5) [1-3] based on the approved WF for the simulation/measurement baseline assumptions [4].
Tentative agreement on PC5 MPR requirements for single carrier (including wide-band) has been suggested during 1st round discussions and supported by a few companies.
This WF is intended to summarize the PC5 MPR requirements and address the open issue on how to handle PC3 MPR requirements.

## Slide 3: Way Forward (1)
Agreement: MPR requirement format to be captured in the specifications.
Modulation |  | MPR (dB) | 
 |  | Full RB allocations | Partial RB allocations
DFT-S-OFDM | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 
CP-OFDM | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 

## Slide 4: Way Forward (2)
Tentative agreement – PC5 MPR requirements for single carrier (including wide-band) are defined as in the following table.
Companies are encouraged to provide further simulation/measurement results to be considered together with the above tentatively agreed MPR values in next RAN4 meeting. The evaluation shall take into account the wide-band operation with ACLR overlapping with IQ image in the non-transmitted sub-channels.
Modulation |  | MPR (dB) | 
 |  | Full RB allocations | Partial RB allocations
DFT-S-OFDM | QPSK | [1.5] | [2.5]
 | 16QAM | [2.0] | [3.0]
 | 64QAM | [3.5] | [4.5]
 | 256QAM | [5.0] | [5.5]
CP-OFDM | QPSK | [3.5] | [3.5]
 | 16QAM | [4.0] | [4.0]
 | 64QAM | [5.5] | [5.5]
 | 256QAM | [7.0] | [7.0]

## Slide 5: Way Forward (3)
Agreements on PC3 MPR requirement evaluations
  Performance requirements applied
    NR-U SEM
    ACLR = 28 dB or 30 dB
    In-band emissions (pending on the WF R4-2008434 for ACLR and in-band emissions)
    EVM
  Both (PC5 + PC5) and PC3 PA configurations are considered.
  (PC5 + PC5) PA configuration reference waveform is the same as with PC5 PA configuration.
  PC3 PA configuration reference waveform is defined as,
    DFT-s-OFDM QPSK 20MHz 100RB3 with 1dB MPR
MPR requirements are down-selected when ACLR requirement is determined at either 28 dB or 30 dB.
FFS on whether one PC3 MPR requirement (worst MPR from the two PA configurations) or two PC3 MPR requirements with capability signaling based on PA configurations will be defined.
Whether (PC5 + PC5) PA configuration MPR requirement is applicable or not is also pending on the outcome of NR Tx diversity requirement discussions.

## Slide 6: References
[1] R4-2007044 “Transmitter characteristics for n46 including initial simulations of required MPR and A-MPR for PC5”, Ericsson, RAN4 #95-e meeting
[2] R4-2008125 “NR-U MPR for PC5 single carrier and wideband”, Qualcomm Incorporated, RAN4 #95-e meeting
[3] R4-2008132 “[NR-U] PC5 and PC3 Back-Off Measurements”, Skyworks Solutions Inc., RAN4 #95-e meeting
[4] R4-2005221 “WF on NR-U UE Tx Requirement”, Skyworks Solutions Inc. et. al., RAN4 #94bis-e meeting