## Slide 1: WF on remaining issues for TS38.101-1 and TS38.101-3 for NR V2X
LG Electronics, Huawei, HiSilicon, CATT
3GPP TSG-RAN WG4#95-e Meeting R4-2009168
Electronic Meeting, 25th May – 05th June, 2020

## Slide 2: Background in TS38.101-1
Most companies would like to complete the NR V2X WI in this meeting to add the NR V2X WI feature in ITU submission.
However, still open issues are listed as follow
  In WF (R4-2008439), A-MPR for PSSCH/PSCCH with NS_52 was not decided.
  In WF (R4-2008440), A-MPR for simultaneous PSFCH for 2 regional regulation were not decided.
  In WF (R4-2008441), A-MPR for S-SSB with NS_33 was not decided.
  In WF (R4-2008446), “General part in TS” is still open how to specify the NR V2X UE RF requirements.
  In draft CR (R4-2008450), there are still existed [ ] in REFSENS and Max. input levels, FFS and Annex A.x.x.

## Slide 3: Background in TS38.101-3
Open issues for con-current operation
  General part: Con-current operation definition
  Output power dynamics
    Intra-band Switching time : [150us]
    Switching period position: Two options
  Delta Rib for V2X_20_n38
    FFS on Delta Rib in B20 by 3rd harmonic problem into n38
  Note: options of the open issues are recorded in WF R4-2008451, these options will be further discussed in next RAN4 meeting.

## Slide 4: WF1: NR V2X completion in RAN4 #95e
For the remaining open issues of NR V2X WI, RAN4 specify the RF requirements with majority view.
The proposed solution will be captured in TS38.101-1 and TS38.101-3 to complete NR V2X WI.
  Remove [ ], FFS, TBD and Editor note
  Reference measurement channel is FFS  Reference measurement channel is A.8
All of listed open issues in the WF, RAN4 will revisit in next RAN4 meeting with technical discussion paper.

## Slide 5: WF2-1: A-MPR for NR V2X UE in TS38.101-1
WF 2-1: A-MPR for PSSCH/PSCCH with NS_52
Carrier frequency(MHz) | Modulation | A-MPR(dB) |  | 
 |  | Region 1 | Region 2 | Region 3
5885 | QPSK | ≤ (10.0 + ΔNote1) | ≤ 8.0 | ≤ 5.5
 | 16QAM |  | ≤ 8.0 | ≤ 5.5
 | 64QAM |  | ≤ 8.5 | ≤ 5.5
 | 256QAM |  | ≤ 8.5 | ≤ 6.0
Note1: Δ is 0, 3, and 5 for 60kHz, 30kHz, and 15kHz SCS, respectively. |  |  |  | 

## Slide 6: WF2-2: A-MPR for NR V2X UE in TS38.101-1
  WF 2-2-1: A-MPR for simultaneous PSFCH with NS_33
  WF 2-2-2: A-MPR for simultaneous PSFCH with NS_52
Channel Bandwidth, MHz | Carrier Frequency (MHz) | A-MPRbase (dB) |  |  | A-MPRstep (dB) | Number of RBs
 |  | 0 ≤ NGap / NRB < 0.15 | 0.15≤ NGap / NRB < 0.3 | 0.3≤ NGap / NRB ≤ 1 |  | 
10 MHz | 5860 | 19 |  |  | 1 | 1
 |  | 22 |  |  | 1 | >1
 | 5870, 5880, 5890, 5900, 5910, 5920 | 5 |  |  | 0.8 | 1
 |  | 14 | 7 | 18.5 | 0.8 | >1
Note 1: NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart) |  |  |  |  |  | 
Channel Bandwidth (MHz) | Carrier Frequency (MHz) | A-MPR (dB)
40 MHz | 5885 | 23.5

## Slide 7: WF2-3: A-MPR for NR V2X UE in TS38.101-1
  WF 2-3: A-MPR for S-SSB transmission with NS_33
Carrier Frequency (MHz) | RBStart * 12*SCS [MHz] | A-MPRBase (dB) | AMPRStep (dB)
5860 | ≤0.54 | ≤ 25 | 1.0
 | >0.54 and ≤3.06 | ≤ 17 | 
 | >3.06 and ≤3.24 | ≤ 11 | 
 | >3.24 and ≤3.6 | ≤ 8 | 
 | >3.6 and ≤7.2 | ≤ 7 | 
5870, 5880, 5890, 5900, 5910, 5920 | ≤0.36 | ≤ 6.5 | 0.5
 | >0.36 and ≤1.44 | ≤ 5.5 | 
 | >1.44 and ≤2.16 | ≤ 4.0 | 
 | >2.16 and ≤3.24 | ≤ 3.0 | 
 | >3.24 and ≤4.32 | ≤ 5.5 | 
 | >4.32 and ≤7.2 | ≤ 6.5 | 

## Slide 8: WF3: Output power dynamics in TS38.101-3
  WF 3: Time mask for TDM operation between NR V2X and LTE V2X at n47 is FFS, not specified in the CR before consensus is reached

## Slide 9: WF4: Delta Rib for V2X_20_n38 in TS38.101-3
RAN4 need to remove FFS in TS38.101-3. In WF (R4-2009170), candidate options are listed as follow
  Option 1: Use the HTF to reduce the 3rd harmonic impact into n38. ΔRIB,c is 0.2dB as use shared pain approach.
  Option 2: Keep the ΔRIB,c is TBD in TR.
  Option 3: A note should be placed either saying “No requirements apply for the case that there is at least one individual RE within the uplink transmission bandwidth of the relative higher band and when the frequency range of relative higher band’s uplink channel bandwidth or uplink 1st adjacent channel bandwidth is fully or partially overlapped with the 3 times of the frequency range of the relative lower band’s downlink channel bandwidth. The reference sensitivity is only verified when this is not the case” or a MSD number should be put into the spec to account for sensitivity degradation when 3rd harmonic of B20 falls into the operating band of n38. A trap filter cannot reduce the 3rd harmonic sufficiently to give only 0.2 dB of REFSENS degradation if a 3rd order harmonic from B20 falls inside band n38.
WF4: In TS38.101-3, RAN4 specify the ΔRIB,c = 0.2dB in Band 20. And MSD level will be specified in next RAN4 meeting.

## Slide 10: WF5: “General part in TS”
RAN4 will further discuss how to specify the general part for NR V2X UE as follow in next RAN4 meeting.
  Option 1
    General requirements apply to V2X (suffix E) unless otherwise stated, so V2X requirements (suffix E) are written only when the requirement differs from the general. This eliminates suffix E clauses.
  Option 2
    For pedestrian-V2X UEs, both the general core requirements and suffix E core requirements apply
    For vehicular UEs supporting the only the NR-V2X sidelink, the suffix E core requirements apply
    Note: At this time the terms ‘vehicular UE’ and ‘pedestrian UE’ have not been defined in the requirements section of the TR, however we anticipate in future this may change.
WF5: Based on the RAN4 agreements, the TS38.101-1 could be revised in next RAN4 meeting.