## Slide 1: WF on BS impact of NR V2X
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, 25 May – 5 June, 2020
Agenda item: 6.4.2
Document for: Approval
R4-2008454
CATT, …

## Slide 2: Background
In RAN4#94-e and RAN4#94-e-bis meeting, the BS impact of NR V2X was discussed but with no agreement reached.
As per the latest WID on NR V2X [1] approved in RAN#87e, the impact on TS 38.104 has been added as indicated below.
In Rel-14, Band 47 is specified in the section of operating bands in both TS 36.101 and TS 36.104.
In current TS 38.104, the co-existence spurious emission requirement is only specified to protect UE Rx in Band 47 for LTE V2X without band n47 for NR V2X.
Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
… | … | … | …
38.101-1 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-2 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-3 | Introduction of NR V2X solutions | RAN#88 | Core part
38.101-4 | Introduction of NR V2X solutions | RAN#90 | Performance part
38.104 | Introduction of NR V2X bands | RAN#88 | Core part

## Slide 3: Frequency band
  Whether or not to specify the frequency band for NR V2X in TS 38.104
    Option 1: To introduce the frequency band for NR V2X in TS 38.104.
    Option 2: No need to introduce the frequency band for NR V2X in TS 38.104.
  Recommended WF: the majority view will be taken in this meeting.
  Qualcomm:Option 1: To introduce the frequency band for NR V2X in TS 38.104.

## Slide 4: Spurious emission
  Whether or not to specify co-existence spurious emission requirement in TS 38.104 for the protection of V2X UE Rx in band n47.
  Option 1: To specify co-existence spurious emission requirement to protect V2X UE Rx in band 47.
  Option 2: No need to specify co-existence spurious emission requirement to protect V2X UE Rx in band 47.
  Recommended WF: the majority view will be taken in this meeting.
  Qualcomm : Option 1 : To specify co-existence spurious emission requirement to protect V2X UE Rx in band 47.

## Slide 5: Reference
[1] RP-200129, Revised WID on 5G V2X with NR sidelink, LG Electronics, RAN#87e
[2] R4-2008303, Email discussion summary for [95e][113] 5G_V2X_NRSL_SysParameters, vivo, RAN4#95-e
[3] R4-1704054, CR on BS for protection of V2X UE in TS 36.104, Huawei, RAN4#82bis
[4] R4-2006260, Discussion on BS impact of NR V2X , CATT, RAN4#95-e
[5] R4-2006264, CR for TS38.104, Introduce BS impact of NR V2X, CATT, vivo, RAN4#95-e