## Slide 1: WF on con-current operation remaining issues
Huawei, HiSilicon
R4-2008451
3GPP TSG-RAN WG4 #95-e
Electronic Meeting, 25 May - 05 June, 2020

## Slide 2: Background
Concurrent operation definition options in 1st round discussion
  Option 1: only the band combination where the Uu schedules/configures SL by semi-persistent way can be specified as concurrent operation (Huawei)
  Option 2: the band combination where the Uu schedules/configures SL can be specified as concurrent operation
  Option 3: the band combinations where the Uu schedules/configures SL can be specified and which is agnostic as to the actual service being delivered on Uu and Sidelink interfaces (LGE, Huawei)
  Option 4: The simultaneous transmission and reception of sidelink and Uu interfaces where operation is agnostic of the service used on each interface (CATT, LGE, Vodafone, Qualcomm).
  Option 4a: the band combination where the Uu interworks with SL can be specified as concurrent operation (vivo)

## Slide 3: Background
Switching time discussion in 1st round
  Option 1: 150us (CATT, LGE, OPPO, Huawei, Futurewei)
  Option 1a: UE capability to indicate the switching time (OPPO)
  Option 2: 210us (Qualcomm)
Switching period position discussion in 1st round
  Option 1: Switching period is placed at the NR slot (CATT, LGE, OPPO)
  Option 1a: see the proposal of Figure 1+ Figure 2b in R4-2007342 (OPPO)
  Option 2: The whole switching time including switching period as well as transient periods shall be placed at the previous E-UTRA sub-frame or NR slot (Huawei, Futurewei, Qualcomm)

## Slide 4: WF on con-current operation definition
Candidate options
  Option a: the band combinations where Uu is capable of scheduling or configuring SL in sidelink resource allocation mode 1 or configuring SL in sidelink resource allocation mode 2
    Note1: Option a) is revised based on option 3 in 1st round.
    Note2: RAN1 is discussing the per band combination UE capability of Uu scheduling/configuring SL. Capable means UE has this capability, but it doesn’t mean Uu has to schedule or configure SL.
    Option 3: the band combinations where the Uu schedules/configures SL can be specified and which is agnostic as to the actual service being delivered on Uu and Sidelink interfaces (LGE, Huawei)
  Option b: The simultaneous transmission and reception of sidelink and Uu interfaces where operation is agnostic of the service used on each interface
    Note3: Option b) is option 4 in 1st round.
    Note4: For TDD synchronous scenario, simultaneous transmission/reception of SL together with Uu DL is not supported according to RAN1 agreement
Suggested WF on con-current operation definition
  Check in 2nd round if option a) is accepted
Conclusion

## Slide 5: WF on switching time
Intra-band Switching time discussion in 1st round
  Option 1: 150us (CATT, LGE, OPPO, Huawei, Futurewei)
  Option 1a: UE capability to indicate the switching time (OPPO)
  Option 2: 210us (Qualcomm)
Suggested WF on switching time
  150us
Conclusion

## Slide 6: WF on switching period position
Switching period position discussion in 1st round
  Option 1: Switching period is placed at the NR slot (CATT, LGE, OPPO)
  Option 1a: see the proposal of Figure 1+ Figure 2b in R4-2007342 (OPPO)
  Option 2: The whole switching time including switching period as well as transient periods shall be placed at the previous E-UTRA sub-frame or NR slot (Huawei, Futurewei, Qualcomm)
  Option 3: Switching period is placed at the last slot/SF of the RAT UE switches from, or placed at the first slot/SF of the RAT UE switches to. Choosing which RAT to place the switching period is up to UE implementation.
  Option 4: Switching period is placed at the first slot/SF of the RAT UE switches to.
Suggested WF
  Further check if one the option below can be accepted
    Option a, the whole switching time including switching period as well as transient periods are placed at low priority LTE or NR SL service
    Option b, revision based on option 1a
Conclusion

## Slide 7
Reference
[1] R4-2006249, Discussion on con-current operation, CATT
[2] R4-2007093, Discussion on current operation scenario and clarification, vivo
[3] R4-2008221, On remaining issues of con-current operation, Huawei, HiSilicon
[4] R4-2006248, Discussion on switching period in ITS band for NR V2X, CATT
[5] R4-2006819, Switching time between NR SL and LTE SL, Qualcomm
[6] R4-2007342, On switching period for LTE SL and NR SL, OPPO
[7] R4-2008219, On switching period for LTE SL and NR SL, Huawei, HiSilicon
[8] R4-2006746, TP on remaining issues for NR V2X UE RF requirements, LGE