## Slide 1: WF on Uplink Full Power Transmission
Samsung
3GPP TSG-RAN WG4#95-e Meeting R4-2008462
Electronic Meeting, 25th May – 5th June, 2020

## Slide 2: Way Forward
Issue 2-1-1: For Uplink Full Power Transmission (ULFPTx) feature in FR2
  UE’s support of full power transmission feature’s mode shall follow RAN1 and RAN2 design;
  If UE claim its support of a mode (from mode-1, mode-2 and the other mode), corresponding performance requirement shall be applied.

## Slide 3: Way Forward
Issue 2-2-1: UE declaring Mode 1 support requirements with DCI 0_0 or single SRS port with DCI 0_1
  For Mode-1 UE, UE is mandated to produce declared full port when it is configured for single SRS port (either with DCI_0_0 or single SRS port with DCI_0_1)
Maximum number of TX antenna connectors:
  For Rel-15 and Rel-16 UE (supporting or not supporting ULFPTx feature), the maximum number of TX antenna connectors is 2.

## Slide 4: Way Forward
For 2 TX antenna connectors with PA1 and PA2, transmit a multi-port SRS resource (i.e., 2TX port) in which both SRS are achieved by PA1+PA2 together:
  Option-1: Not allowed in RAN4 specification
  Option-2: Allowed in RAN4 specification.
  Explanation for the above case:
    For a UE with 2 PA, called as PA1 and PA2, there are following two proposed methods to achieve the above multi-port SRS
      Method-1: SRS port-1 maps to PA1, SRS port-2 maps to PA2
      Method-2: SRS port-1 maps to PA1+PA2, SRS port-2 maps to PA1+PA2
    Method-1 is a straightforward method to be supported, while this question is actually just asking Method-2 can be allowed or not.

## Slide 5: Way Forward
Transparent TxD’s applicability for UEs supporting or not supporting ULFPTx in Rel-16
  [Reconfirm previous agreement] “The applicability of Transparent TxD is NOT related to UE supporting or not supporting Rel-16 ULFPTx”
    [Newly added] In Rel-16, RAN4 requirement needs to allow UE to use transparent TxD to achieve the required transmission power in following cases:
      Mode-1 UE use transparent TxD for single SRS port (either with DCI_0_0 or single SRS port with DCI_0_1)
      Mode-1 UE for two SRS ports:
        Allow or not allow transparent TxD depends on conclusion in previous page.

## Slide 6: Way Forward
Necessity of new RAN4 UE feature for ULFPTx
  RAN4 don’t need to introduce additional UE feature for eMIMO ULFPTx, because the needed UE features have already been introduced or discussed by RAN1.

## Slide 7: Contributions List in RAN4#95-e
T-doc Number | Title | Source | Type
R4-2006494 | MPR With PI/2 BPSK DMRS | Nokia | discussion
R4-2006822 | Pi_2 BPSK DMRS Investigation | Qualcomm Incorporated | other
R4-2008216 | On Pi/2 BPSK DMRS | Huawei, HiSilicon | other
R4-2006345 | On UL Full Power Transmission | Apple Inc. | discussion
R4-2006367 | Discussion on Uplink Full Power Transmission (ULFPTx) | Samsung | discussion
R4-2006368 | CR to TS38.101-1 on introduction of Uplink Full Power Transmission | Samsung | CR
R4-2006369 | CR to TS38.101-2 on introduction of Uplink Full Power Transmission | Samsung | CR
R4-2006668 | [NR_eMIMO] RIMD impact on EVM and MPR for UL MIMO and Tx Diversity | Skyworks Solutions Inc. | discussion
R4-2006779 | CR to clarify UE SRS port configuration for UL tests | Qualcomm Incorporated | CR
R4-2007050 | Verification of FP modes and relation to Rel-15 requirements | Ericsson | other
R4-2007051 | Specification framework for introduction of requirements for the FP modes | Ericsson | other
R4-2007078 | Further on EN-DC and SA power class (Rel-16) | OPPO | discussion
R4-2007079 | CR to TS 38.101-3 EN-DC requirement alignment (R16) | OPPO | draftCR
R4-2008048 | eMIMO FPTX Open items for FR1 | Qualcomm Incorporated | discussion
R4-2008049 | Tx diversity open items for Rel-16 | Qualcomm Incorporated | discussion
R4-2008050 | draft CR to enable FPULTX | Qualcomm Incorporated | draftCR
R4-2008185 | On Release 15 and 16 two Intra-band Transmit Chain Cases | Skyworks Solutions Inc. | discussion
R4-2008217 | On NR eMIMO full power transmission | Huawei, HiSilicon | other
tR4-2008218 | draft CR for TS 38.101-1 eMIMO full power transmission | Huawei, HiSilicon | draftCR

## Slide 8: Reference
[1] R4-2008306, “Email discussion summary for [95e][116] NR_eMIMO_UE_RF”, Samsung