## Slide 1: WF on PC3 intra-band UL CA MPR for GTW
Huawei, HiSilicon
R4-200XXXX
3GPP TSG-RAN WG4 #95-e
May 25th – June 5th, 2020
Electronic meeting

## Slide 2: Background
MPR to be discussed in the GTW session
Intra-band Contiguous UL CA
  Contiguous allocation
    Bandwidth class B
    Bandwidth class C
  Non-contiguous allocation
    Bandwidth class B
    Bandwidth class C
Intra-band non-contiguous UL CA

## Slide 3: Background on inner and outer allocation
Intra-band Contiguous UL CA
Intra-band non-contiguous UL CA
Inner allocation reuses the same concept than single CC allocation of inner half allocation but applied to the 15kHz SCS equivalent aggregated contiguous allocation
For Aggregated channel bandwidth≤200Mhz (class B and Class C)
For RBStart,Low = max(1, floor(NRB_alloc /2)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤ceil[(1/2NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB2*2^µ2
RBStart = RBStart1 ∙ 2^µ1, if LCRB1 > 0
RBStart = NRB1 ∙ 2^µ1 + RBStart2∙2^µ2, if LCRB1 = 0
Other RB allocations are outer RB allocation
Inner allocations are for (IM3 fall within the aggregated channel bandwidth region)
Outer 1 allocations are for (IM3 and IM5 fall in 0 to BW_CA FOOB region: -13dBm/MHz)
Other allocation is Outer 2(there is IMD5 falls into -25dBm/MHz and -30dBm/MHz spurious region)

## Slide 4: Intra-band contiguous UL CA
Contiguous allocation
Table 6.2.3A-2: Maximum Power Reduction (MPR) for Class 3
Modulation |  | MPR for bandwidth class B [dB] |  |  |  | MPR for bandwidth class C [dB] |  |  |  | 
 |  | inner | Avg | outer | Avg | inner | Avg | outer | Avg | Huawei suggestion
DFT-s-OFDM | Pi/2 BPSK | TBD | 0 | TBD | 1.5 | TBD | na | TBD | 6 | 7.5dB
 | QPSK | [0-1.5] | 1 | [2-4] | 3.5 | 2.5 | 2.5 | [5-8] | 6.5 | 
 | 16QAM | [1-2] | 1.5 | [3-4] | 3.5 | 2.5 | 2.5 | [6-8] | 7 | 
 | 64QAM | [2.5-4] | 3 | [3.5-4] | 4 | 5 | 5 | [6-8] | 7 | 
 | 256QAM | [6-6.5] | 5.5 | [6-6.5] | 6 | [6.5-7] | 7 | [6.5-8] | 7.5 | 
CP-OFDM | QPSK | [1.5-2] | 2 | [3-5.5] | 4.5 | [3-3.5] | 3.5 | [6-8] | 7 | 8dB
 | 16QAM | [2-2.5] | 2.5 | [3-4] | 3.5 | 3.5 | 3.5 | [6-8] | 7 | 
 | 64QAM | [3.5-4] | 3.5 | [3.5-4] | 4 | 5 | 5 | [6-8] | 7 | 
 | 256QAM | [6-6.5] | 6.5 | [6-6.5] | 6.5 | [6.5-7] | 7 | [6.5-8] | 7.5 | 
    LTE bandwidth class D MPR and NR single carrier MPR is provide in right side
    For bandwidth B
      the worst case DFT-s-OFDM MPR is not higher than the corresponding LTE bandwidth class D MPR
      CP-OFDM with 2CCs general not larger than single carrier CP-OFDM, at most 0.5dB higher

## Slide 5: WF on Inner and outer contiguous allocation MPR for Class B and C
Modulation |  | MPR for bandwidth class B [dB] |  | MPR for bandwidth class C [dB] |  | 
 |  | inner | outer | Inner | Outer | 
DFT-s-OFDM | Pi/2 BPSK | 1.0 | 3.5 | 2.5 | 7 | 
 | QPSK | 1.0 | 3.5 | 2.5 | 7 | 
 | 16QAM | 1.5 | 3.5 | 2.5 | 7 | 
 | 64QAM | 3.0 | 4.0 | 5 | 7 | 
 | 256QAM | 5.5 | 6.0 | 7 | 7.5 | 
CP-OFDM | QPSK | 2.0 | 4.0 | 3.5 | 8 | 
 | 16QAM | 2.5 | 4.0 | 3.5 | 8 | 
 | 64QAM | 3.5 | 4.0 | 5 | 8 | 
 | 256QAM | 6.5 | 6.5 | 7 | 8 | 

## Slide 6: Intra-band contiguous UL CA
Non-Contiguous allocation
Modulation |  | MPR for bandwidth class B [dB] |  |  |  |  |  |  | MPR for bandwidth class C [dB] |  |  |  |  |  | 
 |  | inner | Avg | Outer1 | Avg | Outer2 | Avg | Huawei Suggestion | inner | Avg | Outer1 | Avg | Outer2 | Avg | Huawei Suggestion
DFT-s-OFDM | Pi/2 BPSK | TBD | 2 | TBD | 5.5 | TBD |  |  | TBD | 2.5 | TBD | 6 | TBD |  | 
 | QPSK | [0-3] | 2 | [4.5-6] | 5.5 | [9-13] | 11 | 13 | [0-5] | 2.5 | [4.5-7] | 6 | [9.5-14] | 11.5 | 14
 | 16QAM | [1-4] | 2.5 | [4.5-6] | 5.5 |  |  |  | [1-5] | 3 | [4.5-7] | 6 |  |  | 
 | 64QAM | [2.5-6] | 4.5 | [4.5-6] | 6 |  |  |  | [2.5-7] | 5 | [4.5-7] | 6 |  |  | 
 | 256QAM | [6.5-7] | 6 | [6.5-7] | 6.5 |  |  |  | [6.5-8] | 6.5 | [6.5-8] | 6.5 |  |  | 
CP-OFDM | QPSK | [1.5-4] | 2.5 | [5.5-8] | 6.5 |  |  |  | [1.5-5] | 3.5 | [5.5-8] | 7 |  |  | 
 | 16QAM | [2-4] | 3 | [5.5-8] | 7 |  |  |  | [2-5] | 3.5 | [5.5-8] | 7 |  |  | 
 | 64QAM | [3.5-6] | 5 | [5.5-8] | 7 |  |  |  | [3.5-6] | 5 | [5.5-8] | 7 |  |  | 
 | 256QAM | [6.5-8] | 7.5 | [6.5-8] | 7.5 |  |  |  | [6.5-8] | 7.5 | [6.5-8] | 7.5 |  |  | 
    LTE bandwidth class D MPR is provide in right side
    Outer 2 allocation MPR value for bandwidth class B is 2-4dB larger than LTE bandwidth class D MPR, according to offline discussion, companies agree to introduce reduced MPR for larger Bandwidth allocation

## Slide 7: WF on Inner and outer non-contiguous allocation MPR for Class B and C
Modulation |  | MPR for bandwidth class B [dB] |  |  | MPR for bandwidth class C [dB] |  | 
 |  | Inner | Outer11 | Outer21 | Inner | Outer11 | Outer21
DFT-s-OFDM | Pi/2 BPSK | 2 | 5.5 | 11.5 for DFT-s-OFDM and 12 for CP-OFDM | 2.5 | 6 | 13 for DFT-s-OFDM and 14 for CP-OFDM
 | QPSK | 2 | 5.5 |  | 2.5 | 6 | 
 | 16QAM | 2.5 | 5.5 |  | 3 | 6 | 
 | 64QAM | 4.5 | 6 |  | 5 | 6 | 
 | 256QAM | 6 | 6.5 |  | 6.5 | 6.5 | 
CP-OFDM | QPSK | 2.5 | 6.5 |  | 3.5 | 7 | 
 | 16QAM | 3 | 7 |  | 3.5 | 7 | 
 | 64QAM | 5 | 7 |  | 5 | 7 | 
 | 256QAM | 7.5 | 7.5 |  | 7.5 | 7.5 | 
NOTE 1: Outer 1 MPR are reduced by 3dB for aggregated allocation bandwidth > 10MHz. Outer 2 MPR are reduced by 4.5dB for aggregated allocation bandwidth > 10MHz |  |  |  |  |  |  | 
This table is applicable to
  1PA architecture for BW class B
  1PA and 2PA architecture for BW class C in Release 16,
  Improved BW class C MPR for 2PA is FFS in future release
  Pi/2 BPSK data is extrapolated from QPSK assuming same ACLR limitation

## Slide 8: Intra-band non-contiguous UL CA
Specify two set of MPR for intra-band non-contiguous UL CA, for 1PA architecture and 2PA architecture respectively
2PA architecture MPR is taken as the 1st priority
Generally, 3dB MPR difference between ENDC and CA
Single MPR for CP-OFDM and DFT-s-OFDM waveforms

## Slide 9
The MPR for intra-band non-contiguous CA For 2PA architecture is defined as below:
  Option 1:keep the worst case with 18dB MPR for low allocation bandwidth
MPRCA =
18 ; 0 < B < 1.08
15 ; 1.08 ≤ B < 2.16
14 ; 2.16 ≤ B < 3.24
13 ; 3.24 ≤ B < 5.4
12 ; B > 5.4
B = 12*(NRB_alloc,1*SCS1 + NRB_alloc,2*SCS2)/1,000,000
Intra-band non-contiguous UL CA-MPR
Option 2: reuse the MPRIM3 defined in 29dBm WI with 3dB difference, which is approved in R4-2006752
MPRCA = 15 ; 0 ≤ B < 1.08
14.5 ; 1.08 ≤ B < 2.16
14 ; 2.16 ≤ B < 3.24
12 ; 3.24 ≤ B < 5.4
11 ; 5.46 ≤ B < 10.8
10 ; 10.8≤ B

## Slide 10: Intra-band non-contiguous UL CA-MPR
  Whether The -13dBm/MHz MPR only used for Band n41 for intra-band non-contiguous CA is defined?
  Option 1: No, -13dBm/MHz is only ASE requirement for USA
  Option 2: Yes (waiting for comments from companies)