## Slide 1: WF on feasibility of testing the transient periods
CMCC
3GPP TSG-RAN WG4 Meeting # 95-e R4-2008477
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background
In RAN#87e meeting, the email discussion on transient period concluded:
- There is no consensus on whether the transient time capability is feasible to test or not. RAN4 CR is 261 is noted. RAN4 continue discussing the feasibility of testing the transient periods in RAN4 during Q2 and report the outcome at RAN#88
In RAN4#94-e meeting, RAN4 discussed the feasibility of testing transient period capability and captured alternatives in WF (R4-2005668)

## Slide 3: WF on testability issues for transient period
Issue 1-1-1: Whether RMS EVM over 1 slot can represent the transient period capability.
Agreements
  Slot level RMS EVM need to be tested even it cannot represent for transient period capability
  No impact on testability

## Slide 4: WF on testability issues for transient period
Issue 1-1-2: For RMS EVM over 1 slot, whether EVM measurement procedure on equalizing is clear for UE
  Option 1: It can be modified when describing EVM procedure for 1 symbol.（Anritsu, QC）
  Option 2: No modifications are required.（Nokia）
  Option 3: no, the equalize procedure can be 1) one DMRS 2) linear interpolation 3) DMRS+ data, it cannot only depend on TE implementation. Whether 1st DMRS can be used for equalization, it will compensate on transient as a part of channel status. The procedure has big impact on whether the EVM measurement is accurate. (HW)

## Slide 5: WF on testability issues for transient period
Issue 1-1-3: For RMS EVM over 1 symbol, how to define EVM measurement procedure in the spec
  Option 1: Adding a new section/annex for EVM to include symbols with transient period. (QC)
  Option 2: It is not an issue whether we create a new section in TS 38.101, we should ensure the procedure could be correct, aligned among TE vendors, high-precision. (Anritsu, HW)

## Slide 6: WF on testability issues for transient period
Issue 1-1-4: Whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change
  Option 1: 20 dB power step is reasonable for on-on power change. (Nokia, QC)
  Option 2: no, power change>20dB is common case under real network. If the reference power change for transient period is 20dB, it will have performance impact on network, if the reference power change for transient period is worst case(e.g.58dB), how UE vendor get known our capability without reliable test environment. (HW)

## Slide 7: WF on testability issues for transient period
Issue 1-1-5: How to ensure the transient period is symmetrically positioned
  Option 1: The exclusion window is defined be symmetric about the symbol boundaries. (Nokia, QC)
  Option 2: Need a baseline on how to position transient period. (HW)

## Slide 8: WF on testability issues for transient period
Issue 1-1-6: Whether EVM=min(EVML, EVMH) can differentiate UE with different transient period ability
  Option1: Do not introduce 1us. For 2us,4us,7us can be further discussed. (QC can accept option1 as a compromise)
  Option2: Including 1us,2us,4us,7us
Agreement
  Do not introduce 1us. For 2us,4us,7us can be further discussed

## Slide 9: WF on testability issues for transient period
Issue 1-1-7: Whether RMS EVM with DFT-OFDM measurement similar with LTE can be tested for transient period
  Option 1: There is not a case that we need to remove the influence of transient period with DFT-s-OFDM symbol during the EVM calculation process. (Anritsu)
  Option 2: no. There is not test on transient period for LTE, 25us exclusion window is specified. The concept cannot be used for transient period test. (HW)

## Slide 10: WF on testability issues for transient period
Issue 1-1-8: UL DL configuration
  Option 1: This issue can be discussed after the testability issues are solved. (Erission, Nokia, QC)
  Option 2: 60 kHz UL DL configuration should be discussed considering blanked symbol is introduced in the current spec.
Agreement
  This issue can be discussed after the testability issues are solved.

## Slide 11: WF on testability issues for transient period
Issue 1-1-9: How to calculate EVM for symbols in which the transient occurs
  Option 1: Test procedure detail that needs to be discussed in RAN5. (Erission, Nokia, QC)
  Option 2: Transient period is different for ramp up and ramp down, it should be clearly clarified. (HW)
Agreement
  This test procedure detail needs to be discussed in RAN5

## Slide 12: WF on testability issues for transient period
Issue 1-1-10: EVM budget for symbol where the transient occurs
  Option 1: Keeping EVM budget in square brackets. EVM values can be discussed after agreement is reached on the feasibility of testing transient periods. (Erission, Nokia, QC)
  Option 2: EVM requirement should decide based on simulation results which can meet network performance on high order modulation. (HW)
Agreement
  Keeping EVM budget in square brackets, and EVM values should be discussed with technical justification after agreement is reached on the feasibility of testing transient periods

## Slide 13: Thanks!