## Slide 1: WF on MPE enhancements
OPPO
3GPP TSG-RAN WG4 Meeting #95-e Draft R4-2008479 Electronic Meeting, May 25-June 5, 2020

## Slide 2: PMPR reporting values
Four options have been provided in this meeting and merged into two options after 1st round. Further down selection is discussed in 2nd round.
  Option A: 2 bits (4 values)
    example value {3 ≤ P-MPR < 6, 6 ≤ P-MPR < 9, 9 ≤ P-MPR < 12, P-MPR ≥ 12}
  Option B: 3-bits (8 values)
    example value {1 ≤ P-MPR< 2, 2 ≤ P-MPR< 3, 3 ≤ P-MPR< 4, 5 ≤ P-MPR< 8, 8 ≤ P-MPR< 12, 12 ≤ P-MPR< 16, 16 ≤ P-MPR< 20, 20 ≤ P-MPR}
It is agreed that PMPR reporting values will be defined with 3 bits.
Note: This is based on the status when this WF is prepared in 2nd round, and status/conclusion will be updated according to the final outcome at comment deadline.
2nd round status @ 3am UTC 3ed Jun | Option1 | Option2
Supporting companies | 3 | 5

## Slide 3: Relative PMPR report trigger threshold
It is agreed that relative PMPR report trigger threshold will be introduced in addition to the absolute P-MPR threshold. (Note1)
It is agreed that relative PMPR report trigger threshold can works below the absolute PMPR threshold. (Note2)
It is agreed that both relative and absolute PMPR report trigger threshold can be used after the first absolute P-MPR threshold based P-MPR report. (Note2)
Note1: This is based on the 1st round status.
Note2: This is based on the status when this WF is prepared in 2nd round, and status/conclusion will be updated according to the final outcome at comment deadline.

## Slide 4: Whether UE needs to report P-MPR = 0dB upon returning to normal operation?
It is agreed that there is beneficial for NW to know UE return to normal operation, but no explicit PMPR=0 reporting is needed. This UE status can be derived implicitly like via P-bit in PHR or relative PMPR reporting, and it is up to implementation.
Note: This is based on the 1st round status.

## Slide 5: Whether UE needs to avoid triggering PMPR report when this PMPR is only temporarily as in current PHR report?
It is agreed that the handling of temporary PMPR is up to implementation.
Note: This is based on the 1st round status.

## Slide 6: Whether it is enough for BS to solve RLF by the reported PMPR itself or need to combine with PHR report?
It is agreed that to solve RLF, PHR information is needed in addition to PMPR and this is limited to FR2.
Note: This is based on the 1st round status.

## Slide 7: Whether periodic reporting is needed?
It is agreed that periodic PMPR reporting is not introduced.
Note: This is based on the 1st round status.

## Slide 8: Whether RAN4 needs to request RAN2 extending/enhance current PHR report to accommodate PMPR reporting?
It is agreed that Whether or not extend/enhance current PHR report to accommodate PMPR reporting is RAN2 issue and will not be discussed in RAN4.
Note: This is based on the 1st round status.

## Slide 9: Where to capture P-MPR report value mapping table?
It is agreed that P-MPR report value mapping table will be introduced in TS38.133.
Further discuss what other aspects need to be captured in 38.101-2 in next meeting.
CRs will be provided in next meeting.