## Slide 1: WF on MPE enhancements
OPPO
3GPP TSG-RAN WG4 Meeting #95-e Draft R4-2008479 Electronic Meeting, May 25-June 5, 2020

## Slide 2: PMPR reporting values
Four options have been provided in this meeting and merged into two options after 1st round. Further down selection is discussed in 2nd round.
  Option A: 2 bits (4 values)
    example value {3 ≤ P-MPR < 6, 6 ≤ P-MPR < 9, 9 ≤ P-MPR < 12, P-MPR ≥ 12}
  Option B: 3-bits (8 values)
    example value {1 ≤ P-MPR< 2, 2 ≤ P-MPR< 3, 3 ≤ P-MPR< 4, 5 ≤ P-MPR< 8, 8 ≤ P-MPR< 12, 12 ≤ P-MPR< 16, 16 ≤ P-MPR< 20, 20 ≤ P-MPR}
=> Both options are equally supported and no conclusion can be reached.
2nd round status | Option1 | Option2
Supporting companies | 6 | 6

## Slide 3: Relative PMPR report trigger threshold
In 1st round, regarding whether relative PMPR threshold is needed in addition to already agreed absolute PMPR threshold, the status is as below.
  => Agreement: Relative PMPR threshold is introduced as a complimentary to the previously agreed absolute P-MPR threshold.
In 2nd round, whether relative threshold can works below the absolute PMPR threshold is discussed, and the outcome is:
  => Agreement: Relative PMPR trigger threshold can works below the absolute PMPR threshold.
=> Agreement: Only absolute PMPR need to be reported.
=> Whether only relative PMPR threshold is used after the first absolute P-MPR threshold based P-MPR report can be further discussed.
1st round status | Option1 (Needed) | Option2 (Not needed)
Supporting companies | 9 | 4
2nd round status | Option A (Yes) | Option B (No) | Concern on relative threshold
Supporting companies | 8 companies | 0 companies | 3 companies

## Slide 4: Whether UE needs to report P-MPR = 0dB upon returning to normal operation?
=> Agreement: There is beneficial for NW to know UE return to normal operation, but no explicit PMPR=0 reporting is needed. This UE status can be derived implicitly like via P-bit in PHR or relative PMPR reporting, and it is up to implementation.
Whether UE needs to avoid triggering PMPR report when this PMPR is only temporarily as in current PHR report?
=> Agreement: The handling of temporary PMPR is up to implementation.

## Slide 5: Whether it is enough for BS to solve RLF by the reported PMPR itself or need to combine with PHR report?
=> Agreement: To solve RLF, PHR information is needed in addition to PMPR and this is limited to FR2.
Whether periodic reporting is needed?
=> Agreement: Periodic PMPR reporting is not introduced.

## Slide 6: Where to capture P-MPR report value mapping table?
=> Agreement: P-MPR report value mapping table will be introduced in TS38.133.
=> Further discuss what other aspects need to be captured in 38.101-2 in next meeting.
=> CRs will be provided in next meeting.
Whether RAN4 needs to request RAN2 extending/enhance current PHR report to accommodate PMPR reporting?
=> greement: Whether or not extend/enhance current PHR report to accommodate PMPR reporting is RAN2 issue and will not be discussed in RAN4.