## Slide 1: WF on FR2 FWA RF requirement
Huawei, HiSilicon, [ ]
R4-2008922
3GPP TSG-RAN WG4 #95-e
May 25th – June 5th, 2020
Electronic meeting

## Slide 2: MBR and BC requirement
In RAN4 #94bis meeting, it is agreed that specify MBR for the new FWA UE, reuse the framework agreed for Rel-16.
  MBR requirement is defined with Per band approach in Rel-16
MBR value per band
  Alt.1-1: 0.7dB per Band for both peak and spherical
  Alt.1-2: 0.5dB per Band as agreed for PC3 in Rel-16
  Alt 1-3: 0dB
Beam correspondence requirement for new FWA UE:
Alt .2-1: define BC bit 0 and 1 requirement for new FWA UE (There is no justification for PC1 not having bit 0, but a newer power class with similar function needing bit 0 relaxation)
Alt. 2-2: Only define BC bit 1 requirement for new FWA Ue
Proposed WF on these 2 requirements:
Adopt Alt.1-3+Alt. 2-1 as a compromise package: define 0dB MBR requirement and define BC bit 0 and 1 requirement for the new FWA UE

## Slide 3: WF on MPRnarrow and minimum output power for the new FWA UE
MPRnarrow for the new FWA UE
  Alt.1 No change from the value defined for PC3
  Alt.2 define MPRnarrow as 7dB for the new FWA UE
Minimum output power for the new FWA UE: -6dBm