## Slide 1: WF on Simulation Assumptions for the SI on 6.425-7.125GHz and 10.0-10.5GHz
Nokia
3GPP TSG-RAN WG4 Meeting # 95-e
Electronic Meeting, 25 May – 5 June 2020
Agenda Item: 11.1
R4-200xxxx

## Slide 2: Background
Contributions on simulation assumptions for the SI on 6.425-7.125GHz and 10.0-10.5GHz in RAN4#95-e:
[1] R4-2006107, “TP to TR 38.9xx: System level simulation methodology and assumptions for study on IMT parameters for frequency ranges 6.425-7.125GHz and 10.0-10.5GHz”, Nokia, Nokia Shanghai Bell.
[2] R4-2007308, “TP on co-existence simulation assumption on 6.425-7.125GHz and 10.0-10.5GHz”, Huawei, HiSilicon.
[3] R4-2007394, “Discussion on simulation assumption for 6425-7125MHz and 10-10.5GHz”, ZTE.

## Slide 3: Way forward on Simulation Assumptions
[Tentative] agreements:
  CLx-ile: CLx-ile = 88 + 10*log10(200/X) + 11 – Y, where X is UL transmission BW (MHz) and Y is the BS noise figure
  SCS: 30kHz
  Scenario to be prioritized: Urban Macro
    Results for other scenarios are still welcome.
  Number of scheduled UE in UL: 1
  BS noise figure: Align with WF in BS parameters
  BS antenna parameters: Align with WF in BS antenna parameters