## Slide 1: WF on RRM requirements for Tx switching between two uplink carriers
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, 25 May – 5 June, 2020
      R4-2008623
Document for: Approval

## Slide 2: Background
It is agreed in RAN4#94e meeting [R4-2002243]:
  DL Interruption requirements due to UL TX switching shall be defined in TS 38.133
    The applicability of DL interruption requirements and if DL interruptions are allowed wait for the conclusion from RF room.
  Switching delay is not specified in TS38.133.
It is agreed in RAN4#94bise meeting [R4-2005416]:
  whether need to capture the applicability for DL interruption requirements in 38.133/36.133.
  Agreement: If the DL interruptions are allowed and the DL interruption applicability is agreed to be captured in RF specification, RRM can directly refer to RF spec. Otherwise, the DL interruption applicability is captured in RRM spec.
  The DL interruption granularity is in the unit of OFDM symbols.

## Slide 3: DL interruption length
DL interruption length
- Option 1
DL Interruption length is
u | NR slot length (ms) of victim cell | UL switching period |  | 
 |  | 35us | 140us | 210us
0 | 1 | 2 | 3 | 4
1 | 0.5 | 2 | 5 | 7
2 | 0.25 | 3 | 9 | 13
No DL interruption is allowed in the downlink carrier(s) which is not indicated by uplinkTxSwitching-DL-Interruption.

## Slide 4: DL interruption length
- Option 2
  DL Interruption length is
 | NR Slot length (ms) | Uplink Tx switching period Note1 |  | 
 |  | 35us | 140us | 210us
0 | 1 | 2 | 3 | 4
1 | 0.5 | 3 | 6 | 7
2 | 0.25 | 4 | 10 | 14
Note 1: Uplink Tx switching period depends on UE capability uplinkTxSwitchingPeriod |  |  |  | 
The above table considers the interruption uncertainty due to MRTD and TA adjustment accuracy, where MRTD=3us.
Interruption length in the above table is expressed by:
  ceil((switching period+2*TA adjustment uncertainty+6us-CP length)/symbol duration)+1
No DL interruption is allowed in the downlink carrier(s) which is not indicated by uplinkTxSwitching-DL-Interruption.

## Slide 5: DL interruption location
The DL interruptions are the OFDM symbols fully or partial overlapped with the UL switching period.

## Slide 6: Others
The IE names in CR [R4-2008624] and [R4-2008625] will be revised according to the RAN2 agreements in the next meeting.