## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #95-e Meeting
Electronic Meeting, 25th May - 5th Jun 2020
R4-2008679

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | No
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | No
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | No
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | No
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | Yes
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | No
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | No

## Slide 3: Agreement
Define requirement for BC bit-0 UE.
  Requirement for BC bit-0 UE is FFS.
Not to define delay requirement when PUSCH/PUCCH and SRS associated with different DL-RSs in one slot

## Slide 4: Way Forward
Whether to consider timing tracking when associated DL-RS?
  Sub1. Whether to consider timing tracking when associated DL-RS QCLed with a different qcl-Type1 RS?
    Option 1:
      No
    Option 2:
      If the spatial relation associated downlink RS is in the active TCI state list, UE shall be able to transmit a PUCCH with target spatial relation at slot n+ THARQ +3 ms/NR slot length
      If the spatial relation associated downlink RS is not in the active TCI state list or unknown, no requirement will be defined.
  Sub2. Whether to consider timing tracking when associated DL-RS is an unknown DL RS?
    Option 1: No
    Option 2: Yes
    Option 3: No requirement will be defined

## Slide 5: Way Forward
When the UL signal has spatial relation to an unknown DL RS,
  Option 1: UE transmits using previous TX beam
  Option 2: Drop UL transmission until TCI state is known
  Option 3: Up to UE implementation and no need to be specified.

## Slide 6: Way Forward
How to deduce the delay requirement for UE which only supports BC Bit-0 when spatial relation is associated with DL RS?
  Option 1: The same delay requirement as BC Bit-1 UE
  Option 2: Always plus the SRS beam sweeping duration compared to BC Bit-1 UE
  Note: The BC Bit-0 UE doesn’t need to meet the same accuracy requirement with Bit-1 for active spatial relation switching.

## Slide 7: Way Forward
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known spatial relation
  Option 1: THARQ +3ms
  Option 2: THARQ +3ms + time for time tracking if applicable
For unknown spatial relation
  Option 1: THARQ + 3ms+ TL1-RSRP
  Option 2: THARQ + 3ms+ TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 8: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known spatial relation
  Option 1: TRRCprocessing
  Option 2: TRRCprocessing + time for time tracking if applicable
For unknown spatial relation
  Option 1: TRRCprocessing + TL1-RSRP
  Option 2: TRRCprocessing + TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes