## Slide 1: WF on NR RRM enhancements – multiple SCell activation
Apple, …
R4-2008994
3GPP TSG-RAN4 Meeting #95-e
Electronic Meeting, 25th May - 5th Jun 2020
Agenda item: 6.15
Document for: Approval

## Slide 2: Requirement scope of multiple SCell activation (Sub-topic 1-1 in R4-2008513)
Agreement in RAN4 #95e:
  RAN4 to not define any requirements for a case where any to-be-activated SCells are unknown without active serving cell or known to-be-activated SCells on the same band

## Slide 3: Scaling for unknown intra-band contiguous being-activated SCell (sub-topic 1-2 in R4-2008513)
Agreement in RAN4 #95e:
  An unknown SCell in FR1 that is contiguous to an active serving cell, or to a known SCell being activated by the same MAC PDU, is not accounted for in, or scaled by, N when the following conditions are fulfilled:
    A single SSB is used in the unknown SCell; or multiple SSBs are used in the unknown SCell and TCI state indication for PDCCH is provided by the same MAC PDU used for SCell activation; and
    its ssb-PositionInBurst is same as the one of FR1 known cell or FR1 active serving cell, and
    its SSB DL Tx beam is same as the corresponding SSB DL Tx beam at the same SSB position of FR1 known cell or FR1 active serving cell, and
    its SMTC offset is same as the one of FR1 known cell or FR1 active serving cell
    Otherwise the SCell is accounted for in, and scaled by, N.
  However, when the following conditions are fulfilled, no activation requirement will be applied for this unknown SCell:
    A single SSB is used in the unknown SCell; or multiple SSBs are used in the unknown SCell and TCI state indication for PDCCH is provided by the same MAC PDU used for SCell activation; and
    its ssb-PositionInBurst is same as the one of FR1 known cell or FR1 active serving cell, and
    its SSB DL Tx beam is different from the corresponding SSB DL Tx beam at the same SSB position of FR1 known cell or FR1 active serving cell, and
    its SMTC offset is same as the one of FR1 known cell or FR1 active serving cell

## Slide 4: “cell detection time” in delay extension due to searcher limitation(sub-topic 1-3 in R4-2008513)
Agreement in RAN4 #95e:
  “Cell detection time” in delay extension due to searcher limitation means “1*TRS” for FR1 unknown SCells and “8*TRS” for the FR2 unknown SCell

## Slide 5: Interruption for multiple SCell activation(sub-topic 1-4 in R4-2008513)
Agreement in RAN4 #95e:
  Single interruption due to RF tuning/retuning shall be assumed when one single MAC CE command is received for multiple SCell activation.

## Slide 6: Multiple SCell activation delay when only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC(sub-topic 1-5 in R4-2008513) (1/3)
Issue 1-5-1: activation delay for FR1 known SCell with Scell_meas_cycle≤160ms
  Agreement in RAN4 #95e:
    TFirstSSB_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell.
    TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell
    TFirstSSB_MAX+ 5ms, for all other cases
Issue 1-5-2: activation delay for FR1 known SCell with Scell_meas_cycle>160ms
  Agreement in RAN4 #95e:
    TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell
    TFirstSSB_MAX + Trs + 5ms, for all other cases

## Slide 7: Multiple SCell activation delay when only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC(sub-topic 1-5 in R4-2008513) (2/3)
Issue 1-5-3: activation delay for FR1 Unknown SCell
  Agreement in RAN4 #95e:
    (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 8*Trs*N2 +Trs +5ms
    where
      N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell. However, an unknown SCell in FR1 that is contiguous to an active serving cell, or to a known SCell being activated by the same MAC PDU, is not accounted for in, or scaled by, N1, when the following conditions are fulfilled:
        A single SSB is used in the unknown SCell; or multiple SSBs are used in the unknown SCell and TCI state indication for PDCCH is provided by the same MAC PDU used for SCell activation; and
        its ssb-PositionInBurst is same as the one of FR1 known cell or FR1 active serving cell, and
        its SSB DL Tx beam is same as the corresponding SSB DL Tx beam at the same SSB position of FR1 known cell or FR1 active serving cell, and
        its SMTC offset is same as the one of FR1 known cell or FR1 active serving cell
        Otherwise the FR1 unknown SCell is accounted for in, and scaled by, N1.
      N2 is the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. If no any parallel to-be-activated SCell on FR2 band, N2 =0. (Moderator: N2 is removed due to agreement in sub-topic 1-1)

## Slide 8: Multiple SCell activation delay when only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC(sub-topic 1-5 in R4-2008513) (3/3)
Issue 1-5-4: activation delay for FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting
  Agreement in RAN4 #95e:
    3 ms + max(Tuncertainty_MAC +TFineTiming + 2ms, Tuncertainty_SP), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell. Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time
    6ms+TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs *N2+ Trs*N1+ TL1-RSRP, measure + TL1-RSRP, report + THARQ + max(Tuncertainty_MAC + TFineTiming + 2ms, Tuncertainty_SP), if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known Scell
      where
      N1 is the number of parallel to-be-activated SCell which is FR1 unknown
      N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. (Moderator: this case is removed due to agreement in sub-topic 1-1)
Issue 1-5-5: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting
  Agreement in RAN4 #95e:
    max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell . Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time
    3ms + TFirstSSB_MAX + 15*TSMTC_MAX + 8 *Trs*N2+Trs*N1+ TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known
      where
      N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell
      N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. (Moderator: this case is removed due to agreement in sub-topic 1-1)

## Slide 9: Multiple SCell activation requirement in inter-band CA in FR2(sub-topic 1-6 in R4-2008513)
Agreement in RAN4 #95e:
  RAN4 to defer the discussion for multiple SCell activation in FR2 inter-band CA