## Slide 1: WF on CSI-RS configuration and intra/inter-frequency measurements definition for CSI-RS based L3 measurement
CATT
3GPP TSG-RAN WG4 Meeting #95e R4-2009002
Electronic Meeting, 25th May – 5th June, 2020

## Slide 2: WF on CSI-RS configuration for measurement requirement
FFS on whether to define requirements for {D=1 with PRBs ≥ 96}.

## Slide 3: WF on CSI-RS based intra-frequency and inter-frequency measurement definition
When CSI-RS resource of serving cell is available
  CSI-RS based intra-frequency measurement: a measurement is defined as a CSI-RS based intra-frequency measurement provided that:
    the SCS of CSI-RS resources on the neighbour cell configured for measurement is the same as SCS of CSI-RS resource on the serving cell configured for measurement, and
    the CP type of CSI-RS on serving cell and target cell is the same, and
      It is applied for SCS = 60KHz
    the centre frequency of CSI-RS resources on the neighbour cell configured for measurement is the same as centre frequency of CSI-RS resource on the serving cell configured for measurement.
  CSI-RS based inter-frequency measurement: a measurement is defined as a CSI-RS based inter-frequency measurement if it is not a CSI-RS based intra-frequency measurement
When CSI-RS resource of serving cell is not available in all configured MOs, no requirements are defined for the MOs configured for CSI-RS based RRM measurement

## Slide 4: WF on requirement for scenarios
Define intra-frequency requirements for the scenarios
  all CSI-RS resources in the same MO have the same BW
  the BW of the CSI-RS on the neighbor cell is within the active BWP of the UE
  No requirement is defined when the BW of intra-MO is different from that of the CSI-RS resources configured for the serving cell in Rel-16
Define inter-frequency requirements for the scenarios
  all CSI-RS resources in the same MO have the same BW
  Inter-frequency CSI-RS resource to be measured with gap that is not confined in the active BWP

## Slide 5: WF on synchronization assumption for CSI-RS measurement
For CSI-RS measurement with associated SSB,
  RAN4 to address the issue of timing difference between the arrival of the CSI-RS and UE’s FFT timing in the performance part