## Slide 1: 3GPP TSG-RAN WG4 Meeting #95-e Electronic Meeting, May 25 – June 05, 2020
Ericsson, […]
WF on Rel-16 MTC RRM requirements
R4-2008641

## Slide 2: Preconfigured UL resource
Do not specify the exact time duration for synchronization and Tserach times for normal DRX and eDRX, instead it is stated that the UE shall be synchronized towards the serving cell prior to the transmission, and otherwise UE shall not transmit (drop or postpone).

## Slide 3: Mobility enhancement: RSS based RSRP measurement for UEs
IDLE mode neighbour cell measurement conditions
  Introduce capability signaling to indicate whether the UE is able to measure on neighbor cell RSS that is in the same NB that UE monitors.

## Slide 4: Mobility enhancement: RSS based RSRP measurement for UEs
CONNECTED mode neighbour cell measurement conditions
  RSS frequency location of the cell being measured occurs in the NB(s) that UE monitors for MPDDCH for the N number of samples
  RSS time location of the cell being measured does not coincide with UE’s measurement gap (if configured)
RSS power offset of the cell being measured is not sRSS location in frequency with respect to measured neighbor cell:
  Follow the similar agreement from IDLE mode
Minimum/maximum distance:
  Follow the similar agreement from IDLE mode
  maller than 0 dB

## Slide 5
Measurement delays in IDLE mode
  RSS-based measurement period is not longer than CRS-based measurement period.
Concurrent CRS and RSS measurements
  The UE is not expected to measure on both RSS and CRS for RSRP measurements.
  In idle mode, UE is not required to concurrently measure based on RSS and CRS.
  UE is required to meet the current CRS based requirements for cells which cannot be measured based on RSS.
  UE is not required to measure both CRS and RSS for the same serving or neighbour cell.

## Slide 6: DL quality reporting
Use the same 2-bit report mapping from Rel-14 NB-IoT for eMTC.
RAN4 reuse the downlink channel quality measurement report mapping of CQI-NPDCCH-Short-NB for eMTC short downlink channel quality report in MAC CE.