## Slide 1: WF on FR2 MIMO OTA (for GTW meeting)
CAICT
3GPP TSG-RAN WG4 Meeting #95-e R4-200xxxx
Electronic Meeting, 25 May – 5 June, 2020
Agenda item: 9.1.1
Document for: Approval

## Slide 2: FR2 MIMO OTA
FR2 PSP Validation procedures
  Whether one polarization is sufficient for PSP validation？
    Suggested WF: vertical polarization validation shall be captured in the TR, further check if horizontal procedure is needed.
  Whether the proposed radius of 5cm validation procedure is sufficient？
    Suggested WF: adding radius of 5cm procedure in the TR with additional statement that the considering the suitable testing time 5cm procedure is adopted. PSP validation with radius of 10cm is FFS.
    Further comparison among 5cm and 10cm results will be discussed in the future i.e. WI phase.
  Further check if we need to specify the reference antenna in the future i.e. WI phase
FR2 Dynamic testing (Beam Switching/Refinement testing)
  Step one: The group shall make decision, do we need an additional new MIMO requirement to identify the UE performance under Beam switching/refinement stage？
    Option 1: YES
    Option 2: No (Huawei)
    Option 3: Further study in the Rel-17 WI (Sprient, keysight, Qualcomm)
    Option 4: Further study dynamic test in a sperate SI in future release (keysight, Huawei, Samsung, Oppo, Sprient, CAICT,Qualcomm)
  Step two: If option 1 is agreed. What proper performance metric shall be for this new test case？
    Option 1: Averaged throughput in T2 time window (i.e. the time between UE rotation and stable maximum Throughput condition)?
    Option 2: Absolute Time before reaching [xx]% of maximum throughput in T2?
    Option 3: Throughput vs Time curve with other KPI?
    Other ideas?
  If no consensus: What is the next step for this topic?
    Option 1: New SI for T2 and “real” dynamic testing
    Option 2: Further study in Rel-17 MIMO OTA WI
    Option 3: no guidance from RAN4
    Other ideas?
  Agreement: NO conclusion in Rel-16 MIMO OTA test SI.
Notes: Keysight：support WF, both works but simply just use one.
QC: How to compare to 5cm with 10cm, what’s the criteria?
R&S: same question as QC.
Keysight: we have show results.
Samsung: It’s not ready to accept this test case without enough research.
This semi-dynamic scenario not match realistic scenario. Also static MIMO test system maybe not suitable. We prefer to have a new SI to introduce a real dynamic test cases which more pratical.
QC: This is not RRM test case, it’s T-put test cases. We also aware this not real dynamic test case we comprised in T2 window.
We would like to further discuss in WI phase.
Huawei: Q1: during T2 time window, do we really have demod requirements corresponding channel model?
Q2: Maximum input level in OTA test during T2 window, how we can reach such conditions.
Our preference not to introduce.
Oppo: not a use case for the proposed test case? T2 time window not proper time window.