## Slide 1
3GPP TSG-RAN WG4 Meeting #95-e R4-2008820
Electronic Meeting, 25 May – 5 June, 2020
Agenda Item: 6.17.2.1
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS
  R4-1915926 WF on UE demodulation for NR HST, RAN4#93
  R4-2002418 WF on UE demodulation for NR HST, RAN4#94-e
  R4-2005532 WF on UE demodulation for NR HST, RAN4#94bis-e

## Slide 3: HST single tap
Maximum Doppler frequency
  For 15KHz SCS, 500km/h
    Option 1 (Intel, Huawei): 870Hz
    Option 2 (Huawei, CMCC, Ericsson, DOCOMO, Qualcomm): 972Hz (Same as LTE HST 500km/h doppler frequency)
Agreement:
Using 972Hz to define UE requirements
RAN4 also aware that with this agreements, the maximum Doppler frequency not aligned between BS and UE requirements in Rel-16 HST WI.
This value is not maximum values of Doppler frequency on UE side which UE can support

## Slide 4: HST single tap
The assumption of HST single tap requirements
  Background
    Do not mandate the specific TRS processing for requirement definition and left it up to company decision(agreement in last meeting)
    For HST single tap requirements, no capability signalling will be introduced (last meeting agreement), and the requirements is mandatory (agreement in 1st round)
  Open issue
    whether to provide signalling during the HST single tap demodulation test
      Option 1 (Huawei, Ericsson, DOCOMO, CMCC, Qualcomm): Do not provide signalling during the HST single tap demodulation test
      Option 2(Intel): Provide HST RRM signalling during the demodulation test as additional indication of HST conditions
Agreement:
  No conclusion in Rel-16 for this issue, RAN4 open to further discuss the signaling issue in the future releases.

## Slide 5: Transmission scheme
For DPS transmission scheme(including 1a and 1b), whether new specific UE receiver processing from demod aspect required compared to UE to handle HST-single Tap and HST-SFN channel model
  Agreement in 1st round
    Frequency error tracking of Large Doppler shift jump in DPS cannot be verified in HST single tap.
    TCI state switch in DPS cannot be verified in HST single tap and HST-SFN
  Open issue in 2nd round
    Whether the frequency error tracking can be verified in HST-SFN
    Whether TCI state switch can be verified in multi-TRP transmission requirements discussed in eMIMO

## Slide 6: Transmission scheme
Whether to define new requirements and tests for DPS transmission scheme
  Option 1: Do not consider Transmission schemes 1 for defining new requirements.
  Option 2b: Define performance requirements for DPS 1a and 1b with test applicability rule for different UE capabilities. If UE supports more than one active TCI state (2 or 4) the requirements with lower number of active TCI states can be skipped. If UE passed HST-SFN requirements it does not need to be tested in HST-DPS.
  Option 2c: Define performance requirements for DPS 1a and 1b with test applicability rule for different UE capabilities. If UE supports more than one active TCI state (2 or 4) the requirements with lower number of active TCI states can be skipped.
Agreement:
  Introduce test cases for DPS transmission schemes 1a ; FFS for 1b
  Define RAN4 requirements with the assumption of frequency tracking up to UE implementation.
  In test cases, TCI states know to UE (FFS for detailed test case set-up)
  FFS for test applicable rule among 1a/[1b] with HST-SFN requirements

## Slide 7: Transmission scheme
Test setup for transmission scheme 1a
  Use following as baseline for DPS transmission scheme 1a test setup if it is agreed to introduce DPS test (agreement in 1st round)
    UE is configured with two different TCI states associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
    TE actives TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE”;
    PDSCH associated with TCI #0 is transmitted during the slots from 0 to (n-1) + HARQ needed time + 3ms + first TRS + TRS processing time;
    In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
    PDSCH associated with TCI #1 is transmitted in slots from n + HARQ needed time + 3ms + first TRS + TRS processing time to N.
    where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH

## Slide 8: Transmission scheme
Test setup for transmission scheme 1b
  Use following as baseline for DPS transmission scheme 1b test setup if it is agreed to introduce DPS test (agreement in 1st round)
  for scenario with 2 active TCI states
    (total 2 active TCI states): PDCCH TCI state switching delay caused by MAC CE, but less than DPS 1a with pre-tracking of second TCI state and only HARQ needed time + 3ms delay is needed, UE tracks 2 active TCI states in advance so that UE can quickly get better Doppler shift estimation for the second TRP compared to DPS 1a.
    UE is configured with two different TCI states (TCI #0 and TCI #1) associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
    TE activates TCI #0 and TCI #1 for PDSCH at the same time by “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” and activates TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE” command with the field of CORESET ID set to 0;
    TE transmits PDCCH and PDSCH associated with TCI #0 from TRP#1 from slot 0 to n-1;
    In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
    TE transmits PDCCH and PDSCH associated with TCI #1 from TRP#2 from slot n to N.
    where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH

## Slide 9: Transmission scheme
Test setup for transmission scheme 1b
  Use following as baseline for DPS transmission scheme 1b test setup if it is agreed to introduce DPS test (agreement in 1st round)
  for scenario with 3 active TCI states
    (Total 3 active TCI states): No PDCCH TCI state switching delay by using MAC CE, but 3 active TCI states to track, UE needs to report supporting of maxNumberActiveTCI-PerBWP = n4
    UE is configured with three different TCI states (TCI #0, TCI #1 and TCI #2) associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config;
    TE activates TCI #0 and TCI #1 for PDSCH at the same time by “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” and activates TCI #2 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE” command with the field of CORESET ID set to 0;
    TE transmits PDCCH associated with TCI#2 from TRP#1 and TRP#2 from slot 0 to N
    DCI contains pointer to TCI#0 from slot 0 to n-1 and pointer to TCI#1 from slot n to N
    TE transmits PDSCH associated with TCI #0 from TRP#0 from slot 0 to n-1
    TE transmits PDSCH associated with TCI #1 from TRP#1 from slot n to N
    where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH

## Slide 10: UE capabilities/features
  For HST fading channel requirements and HST single Tap channel demodulation requirements
  Background:
      For HST fading channel requirements take it as mandatory requirements for Rel-16 and no capability signaling will be introduced.(agreement in last meeting)
      For HST single Tap channel demodulation requirements
        no capability signaling will be introduced (agreement in last meeting)
        requirements is mandatory (agreement in 1st round)
  Open issue:
    Whether feature list will be introduced for HST fading channel, and HST single tap

## Slide 11: Applicability rule
Test applicability between HST-SFN, HST single tap and HST multi-path fading performance test cases
  Option 1: Do not define any applicability rules between HST-SFN, HST single tap and HST multi-path fading performance test cases.
  Option 2: Do not test UE under HST single-tap, if UE passes the requirements for HST-SFN.
    Alt 1: Skip the Rel-15 HST single tap test, if UE passes the requirements for HST-SFN
    Alt 2: Skip the Rel-16 HST single tap test, but do not skip the Rel-15 HST single tap test, if UE passes the requirements for HST-SFN
    Alt 3: Skip both Rel-15 and Rel-16 HST single tap test, if UE passes the requirements for HST-SFN

## Slide 12: Applicability rule
Test applicability between different Doppler frequencies for the same channel model
  Agreement in 1st round: For HST single tap: UE can skip Rel-15 HST single tap test if UE has passed the Rel-16 HST single tap case
  Open issues in 2nd round
    For FDD:
      Option 1a: Rel-15 multi-path fading with TDLB100-400 (Table 5.2.2.1.1-3 Test 1-1 and Table 5.2.3.1.1-3 Test 1-1) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-600 for FDD
      Option 1b: Rel-15 multi-path fading with TDLC300-100 (Table 5.2.2.1.1-3 Test 1-2 and Table 5.2.3.1.1-3 Test 1-2) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-600 for FDD
      Option 2: Not define any applicability rule for FDD multi-path fading tests between Rel-15 and Rel-16.

## Slide 13: Applicability rule
Test applicability between different Doppler frequencies for the same channel model
  Open issues in 2nd round
    For TDD:
      Option 1a: Rel-15 multi-path fading with TDLB100-400 (Table 5.2.2.2.1-3 Test 1-1 and Table 5.2.3.2.1-3 Test 1-1) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-1200 for TDD.
      Option 1b: Rel-15 multi-path fading with TDLC300-100 (Table 5.2.2.2.1-3 Test 1-2 and Table 5.2.3.2.1-3 Test 1-2) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-1200 for TDD.
      Option 2: Not define any applicability rule for TDD multi-path fading tests between Rel-15 and Rel-16.

## Slide 14: HST-SFN
Maximum Doppler frequency
  For FDD 15 KHz SCS, 500km/h
    870Hz
      larger implementation margin of 1 dB instead of 0.5dB being added on top of average impairment simulation results
      No conclusion on whether to use +/-0.1ppm frequency error margin when determining maximum Doppler frequency for HST-SFN

## Slide 15: Release independent
Whether Rel.16 HST requirements can be release independent from Rel-15
    Rel.16 HST requirements, including HST single tap and multi-path fading are release independent from Rel-15
      The requirements for Rel-16 HST single tap and multi-path fading test are optional for Rel-15 UEs
    RAN4 wait for the LS response from RAN2 to decide whether Rel-16 HST-SFN requirement is released independent from Rel-15 or not

## Slide 16: Updated simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 870Hz Option 2: 851Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 17: Updated simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1×2; 1×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1250Hz Option 2: 870Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 18: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15