## Slide 1: WF on IAB-MT output power dynamic
Qualcomm Incorporated
R4-2008775
3GPP TSG-RAN WG4 Meeting # 95-eis
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background
Dynamic range should guarantee that IAB-MT to parent link can maintain a certain level of performance under different conditions
  Fading/shadowing, weather variation, etc

## Slide 3: Way Forward
Dynamic range can be expressed as X+10*logNRB
  X is given in the next slides
  NRB is the maximum number of RBs that can be configured in the channel
How to capture the dynamic range in the spec is FFS

## Slide 4: Way Forward
For WA IAB-MT
  FR1 – X= [10]dB
  FR2 – X= [10]dB
For LA IAB-MT
  FR1 – X= [10]dB
  FR2 – X=[10]dB

## Slide 5: Way Forward
For IAB-MT transmitting in DL slots or with SDM/FDM operation:
  This operating mode is based on implementation, the dynamic range in slide 3 is the minimum requirement to maintain backhaul link performance
  IAB-MT can support larger dynamic range if needed for specific deployments