## Slide 1: WF on BS demodulation requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 Meeting #95-e
E-meeting, 25th May – 5th Jun, 2020
R4-2008864

## Slide 2: Background
Agreed WFs in previous meetings (Newest first)
  RAN4#94bis-e
    R4-2005555 WF on BS demodulation performance requirements for 2-step RACH
  RAN4#94-e
    R4-2002389 WF on BS demodulation requirements for 2-step RACH

## Slide 3: Agreements from the first round discussion(1)
TO Compensation is assumed when specifying BS demodulation requirements for 2-step RACH for WA and MR BS. For LA BS, FFS whether T0 compensation is assumed (examing impact of T0 compensation first)
Excluding 0µs TO
Using “4-step RA type” and “2-step RA type” aligned with RRM session and RAN2 for the discussion and specs texts if necessary

## Slide 4: Agreements from the first round discussion(2)
The following setup acceptable for specifying BS demodulation requirements for 2-step RACH:
  Not limiting preamble format
  No re-transmission assumed
  Not specify power offset between preamble and PUSCH/MsgA in the specification and allow TE vendor to decide it during the test with always correct preamble decoding
  1T2R
  TDLC300-100 for FR1, TDLA30-300 for FR2
  SNR on PUSCH/MsgA
  SCS: 15k and 30k for FR1, 60k and 120k for FR2, but only one SCS can be tested
  DMRS configuration 1+1+1 or 1+1 based on evaluation results.
  TB size 56-72 bits, subject to changes with the selection of MCS, PRB number and symbol number, assuming the least padding bits
  Consider MCS level, PRB number and symbol number together, and start with MCS1, 2 PRBs and 14 symbols for FR1, MCS 3, 2 PRBs and 10 symbols for FR2, but leaving other options open

## Slide 5: Agreements in the second round discussion
Introduce TO cycling (X, ∆t, Y) in defining core requirements
Introduce different sets of (X, ∆t, Y) for different SCS for cases where the X, Y relate to CP length
Introduce High and medium level TO sets
FFS if different High and medium level TO sets are necessary
Do not define requirements with low level TO values. Write note in specification that 2-step RACH performance requirements are applied only to WA and MA BS types. Demodulation performance for LA BS can be guaranteed without performance testing. Clarify in specifications that LA BS can operate 2-step RACH without meeting additional performance requirements.
BS may declare its support to which TO level if multiple levels

## Slide 6: Way forward (1) – TO compensation
Further study difference in UE TO compensation implementation for high and medium TO values (outside and outside the CP). If essential difference will be observed – requirements will be defined for both. Otherwise only for high level.

## Slide 7: Way forward (2) Medium level TO cycling
Use the following values as a baseline for medium level TO cycling for the performance evaluation
Revised values may be proposed next meeting
Range /Cycles | 15 kHz SCS |  |  | 30 kHz SCS |  |  | 60 kHz SCS |  |  | 120 kHz SCS |  | 
 | X | ∆t | Y | X | ∆t | Y | X | ∆t | Y | X | ∆t | Y
Medium level | 0.8 | 0.2 | 2 | 0.4 | 0.1 | 1 | 0.2 | 0.05 | 0.5 | 0.1 | 0.025 | 0.25

## Slide 8: Way forward (3) High level TO cycling
Companies are encouraged to provide more inputs justifying the preferred high level TO values.
  Y should be related to maximum cell size and may be greater than the CP length
  FFS whether or not Y > CP
Range /Cycles | 15 kHz SCS |  |  | 30 kHz SCS |  |  | 60 kHz SCS |  |  | 120 kHz SCS |  | 
 | X | ∆t | Y | X | ∆t | Y | X | ∆t | Y | X | ∆t | Y
High level |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Way forward (4) – PUSCH mapping type
PUSCH Mapping type
  Option 1: Type A for FR1, Type B for FR2
  Option 2: both Type A and Type B for both FR1 and FR2
  Option 3: both Type A and Type B for FR1, Type B for FR2
  Option 4: only for the mapping type declared to be supported in D.100. If both mapping type A and type B are declared to be supported, the tests shall be done for either type A or type B.

## Slide 10: Way forward (5) – Test metric
Test metric: BLER of MsgA when preambles are correctly detected
  Option 1: 0.01
  Option 2: 0.1

## Slide 11: Simulation setup
Parameter | Values for FR1 |  | Values for FR2 | 
Preamble format | Free choice |  |  | 
Waveform | CP-OFDM |  |  | 
Power offset between preamble and MsgA | Free choice |  |  | 
Subcarrier spacing for PUSCH | 15kHz, 30kHz |  | 60kHz, 120 kHz | 
PUSCH Mapping Type | Option 1: Type A and Type B Option 2: Type A |  | Option 1: Type A and Type B Option 2: Type A | 
MCS level | 1 |  | 3 | 
Number of symbols | 14 |  | 10 | 
Number of PRBs | 2 |  | 2 | 
TBS | 56 - 72 bits |  |  | 
DMRS | Option 1: 1+1+1 Option 2: 1+1 |  | Option 1: 1+1+1 Option 2: 1+1 | 
Antenna configuration | 1T2R |  | 1T2R | 
Propagation channel | TDLC300-100 |  | TDLA30-300 | 
TO values | Medium level | SCS 15k: 0.8:0.2:2 | Medium level | SCS 60k: 0.2:0.05:0.5
 |  | SCS 30k: 0.4:0.1:1 |  | SCS 120k: 0.1:0.025:0.25
 | High level | TBD | High level | TBD
Test metric (BLER of MsgA when preambles are correctly detected) | - Option 1: 0.01 - Option 2: 0.1 |  | - Option 1: 0.01 - Option 2: 0.1 | 
Re-transmission | No retransmission considered |  |  |