## Slide 1: WF on support of 30k SCS for SSB of n34, n38, n39 and n50
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #95e
Online, 25th May – 5th June, 2020
R4-2008386

## Slide 2: Background
  Since RAN4#94e-bis the issue on whether 30KHz SSB SCS should be supported on band n34, n38, n39, and n50 were discussed.
    The summary for RAN4#94e-bis was provided in R4-2005685.
    The summary for 1st round discussion in RAN4#95e was provided in R4-2008291.
  According to summary in R4-2008291, the status of the discussion is
    For n38 and n39
      For n38 and n39, majority views go for adding 30k SCS support to SSB with Case C sync pattern, but there is a strong concern on the increased complexity due to dual default SSB SCSs.
        Aligning n38 and n41 may also lead to revisiting dual SSB SCSs for n41.
      For n38, the operator propose keeping 15KHz SSB SCS to align with 15KHz data SCS
      For n39, the operator and vendors proposed keeping 15KHz SCS to support 5MHz channel bandwidth in Japan.
  For n34,
      For n34, agree to add 30k SCS to SSB with Case C sync pattern and keep 5MHz minimum channel bandwidth. The reason is that the increased complexity due to dual SSB SCSs is acceptable since the bandwidth of n34 is only 15MHz.
  For n50
    For n50, agree to replace 15k SCS with 30k SCS to SSB with Case C sync pattern, and keep 5MHz minimum channel bandwidth but not self-discoverable

## Slide 3: Way forward
  For n34 and n39
    SSB SCS:
      Alt a.
        Add 30KHz SCS support for n34 and n39 SSB, thus support both 15KHz and 30KHz SCS
      Alt B:
        Do not change SSB SCS
    SSB pattern for 30KHz SCS:
      Case C

## Slide 4: Way forward
  For n38
    SSB SCS:
      Add 30KHz SCS support for n38 SSB, thus support both 15KHz and 30KHz SCS, and find a way to limit GSCN for 30KHz and/or 15KHz SSB SCS especially for 5MHz based on expected n38 deployment.
    SSB pattern for 30KHz SCS:
      Case C

## Slide 5: Way forward
  For n50
    SSB SCS:
      Replace the current 15KHz SCS with 30KHz SCS for n50 SSB
      Keep the current 5MHz but a cell with 5MHz channel bandwidth will become not self-discoverable
    SSB pattern for 30KHz SCS:
      Case C