## Slide 1: 3GPP TSG-RAN WG4 Meeting RAN4#95-e R4-2008404 Online, May 25 – June 5, 2020
WF on EVM Requirement for UL MIMO Transmission
Motorola Mobility

## Slide 2: Background
For single antenna transmission
  Tx EVM is specified at the antenna connector in TS 38.101-1
  Tx EVM at the antenna connector is the same as the EVM per layer for single antenna transmission
For UL-MIMO, two layers are transmitted from two antennas
  Tx EVM at each antenna connector is not the same as the EVM per layer and it is EVM per layer that determines the noise/error floor for the transmission layer
  To specify and measure EVM per layer due to transmitter impairments, a MIMO receiver is needed

## Slide 3: Way Forward
Consider methods for defining and measuring per-layer EVM for UL MIMO transmission
  Methods that can be considered should include at least
    Linear MMSE MIMO Receiver
    Linear Zero-Forcing MIMO Receiver
  Evaluation of methods may include at least per-layer EVM as a function of
    The channel matrix H
    The variance and cross-correlation of the Tx noise at the antenna connectors; e.g.,
  with correlation matrix σ2
  Note: UL-MIMO EVM is to be tested with both layers transmitted; i.e. 2-layer UL MIMO transmission with codebook

## Slide 4: References
[1] R4-2008057, ’On the Transmit EVM Requirement for UL MIMO Transmission,’ Motorola Mobility, 3GPP TSG-RAN WG4 Meeting #95-e, May 2020.
[2] R4-2006777, ’ CR to 38.101-1: Revision to ULMIMO EVM spec,’ Qualcomm, 3GPP TSG-RAN WG4 Meeting #95-e, May 2020.
[3] R4-2008214, ’ On UL MIMO Tx EVM requirement,’ Huawei, 3GPP TSG-RAN WG4 Meeting #95-e, May 2020.
[4] R4-2004866, ‘FR1 TX EVM test condition correction for ULMIMO,’ Qualcomm, 3GPP TSG-RAN WG4 Meeting #94-e-Bis, April 2020.
[5] R4-2004791, ‘EVM Definitions for Antenna Ports and MIMO Layers,’ Motorola Mobility, 3GPP TSG-RAN WG4 Meeting #94-e-Bis, April 2020.
[6] R4-2004734, ‘On UL MIMO Tx EVM requirement,’ Huawei, 3GPP TSG-RAN WG4 Meeting #94-e-Bis, April 2020.
[7] R4-2000204, ‘FR1 TX EVM test condition correction for ULMIMO,’ Qualcomm, 3GPP TSG-RAN WG4 Meeting #94-e.
[8] R4-1913226, ‘TX EVM test condition correction for ULMIMO,’ Qualcomm, 3GPP TSG-RAN WG4 Meeting #93, Reno, NV, USA, Nov 2019.