## Slide 1: WF on Power Class related UL MIMO and other requirements
vivo
3GPP TSG-RAN WG4#95-e Meeting R4-2008408
Electronic Meeting, 25 May – 5 June., 2020

## Slide 2: Way Forward(1)
Package solution for Sub-topic 1-1 (TxD and power-capability indication for SA operation)
  Option 1:
    Setting up TxD requirements in Rel-16 and Release independent from Rel-15;
    Do not allow SA SU indicating PC2 fallback to PC3 for 1-port transmission;
  Option 2:
    Setting up TxD requirements for TxD in Rel-16; Not allow to release independent from Rel-15;
    Allow SA UE indicating PC2 fall back to PC3 for 1-port transmission;
  Option 3:
    Setting up TxD requirements for TxD in Rel-15;
    Allow SA UE indicating PC2 fall back to PC3 for 1-port transmission;
  Option 4:
    Setting up TxD requirements for TxD in Rel-16; Not allow to release independent from Rel-15;
    Do not allow SA UE indicating PC2 fall back to PC3 for 1-port transmission;
  Option 5
    Decide release independence once requirements are agreed
  Option 6:
    Decide release independence once TxD requirements are agreed
    Allow SA UE indicating PC2 fall back to PC3 for 1-port transmission in R15;
  Option 7:
    Setting up TxD requirements in Rel-16 and Release independent from Rel-15;
    Allow SA UE indicating PC2 fall back to PC3 for 1-port transmission in R15;
    Add capability signaling in R16 to distinguish between 23+23dBm and 26dBm implementations. Such signaling nee ds to be usable by R15 UEs too
      Maybe the existing R15 1PA/2PA signaling can be reused already
      Will the network be able to implement the R16 capability for R15 UEs?
      Is this for intra-band EN-DC or inter-band EN-DC, or both?
      Needs to have all the requirements in a CR to better under the whole option
  [Note: Option 3&4 is not likely to be agreed and it is proposed to focus on Option 1 or Option 2. ]

## Slide 3: Way Forward(2)
For R15 UL MIMO emission requirements, using R4-2008046 (Qualcomm) as a baseline;
  Focus on 2-layer requirements;
  Both PC2 and PC3 were considered;
Interested companies can provide MPR measurement results for further check in RAN4#96-e
  [The assumptions could be…]
MPR of Rel-15 UE for 1Tx should not be affected in any case

## Slide 4: Way Forward(3)
For the current REl-15 RAN4 clarification of NSA NR power class
  Option 1: Keep it as it is;
  Option 2: Revert the clarification by deleting it.
  …
How to treat the Rel-16 NR power class in MR-DC mode
  Option 1: Introduce explicit signaling;
  Option 2: Not introduce signalling, no further change;
  Option 3: Introduce the current Rel-15 changes;
  …

## Slide 5: Way Forward(4)
[Further discuss the need for CDD based TxDiv evaluation]
[EVM measurement for TxD case]
  [Confirmed with other TxD discussion]

## Slide 6: Reference
[1] R4-2008935, Email discussion summary for [95e][104] NR_NewRAT_UE_RF_Part_3, Moderator (vivo), RAN4#95-e