## Slide 1: WF on WRC-19 outcome and impact on RAN4 specifications
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #95-e R4-2008410
Online Meeting, 25 May - 5 June 2020

## Slide 2: Background (1/3)
Common understanding of which regulatory requirements TS38.101-2 should address (for information only):
  Note: Necessity of -8dBm/200MHz is FFS.
  Note: Some must be met simultaneously like 1/2/4 and 1/3/4 for Europe.
Region3/ | Requirement 1 | Requirement 2 | Requirement 3 | Requirement 4 | Requirement 5 | Requirement 6
Global, US, Japan | Protected range: spurious Band applicability: all Limit: -13 dBm/MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: +1 dBm/200 MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: -5 dBm/200 MHz | N/A | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: +7 dBm/1000 MHz | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: -13 dBm/1 MHz
Europe |  |  |  | Protected range: 7.25 GHz ≤ f ≤ 2nd harmonic Band applicability: all bands Limit: -10 dBm/100 MHz |  | 

## Slide 3: Background (2/3)
To introduce the regulatory requirements in TS 38.101-2, the following issues have been discussed.
  Connectivity issues when adding new NS values to existing bands [1][2][3]
  Handling of regulation to change from a loose limit to stringent one with transition period [3]
    Invoked larger A-MPR from the changeover date
    Allows UEs violating regulation to work if the NS value for stringent one is optional support
  NS value mapping and A-MPR issues [3]

## Slide 4: Background (3/3)
Agreements from WF [3] in RAN4#94-e-bis (This is an extract, the details are described in [3])
  The followings are package agreements.
    How to resolve the issues identified in the background slides
    NS mapping and associated A-MPR
      After the process on how to resolve the newly introduced NS issues and NS mapping is agreed, each band will be handled independently without waiting for the completion of the other bands.
  A feature for a UE to report newly supported NS value(s) for a legacy band to a network is introduced. Four Alts are listed.
    Alt 1-1: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network (introduce a new signaling feature)
    Alt 1-2: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network (reuse modifiedMPR bits)
    Alt 1-3: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network, such that supporting of NS values is optional
    Alt 2: Delay introduction of new NS until beginning of Rel-X, such that it is mandatory for a UE designed against Rel-X to support all NS values defined in the Rel-X version of the specification and which correspond to the bands which the UE supports.
  For NS mapping and A-MPR,
    Adopt one of the two (Option 1 or 2 in [3]) based on necessity of -8dBm/200MHz.
    +1dBm/200MHz for n257 & 7dBm/1GHz for n259 are introduced into NS_200, respectively, at least if no A-MPR is needed.
    The same mapping for single CC is applied to that for CA.
    A note is added to NS values for changed emissions limits (example shown: -5dBm/200MHz after 1st Sep 2027 in [3])

## Slide 5: Option 1: -8dBm/200MHz stays
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | -8dBm/200MHz + -10dBm/100MHz | -8dBm/200MHz + -10dBm/100MHz |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
NS_206 | -5dBm/200MHz + -10dBm/100MHz | -5dBm/200MHz + -10dBm/100MHz |  | 
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.
Notes: Qualcomm: (removed -10/100 from NS_201). Supporting -10/100 requirement will require higher AMPR for NS_201 relative to v16.3. Devices that support exist NS_201 already exist. At this time we do not support repurposing an existing NS unless we are running out of NS flags for a band.
We ask if companies can check if NS_206 is required as a standalone NS. We think NS_202 has enough AMPR to support -5 dBm/ 200 MHz due to compliance with -10/100. So NS_206 is not required for EU, post 2023, based on existing view of emissions requirements

## Slide 6: Option 2: -8dBm/200MHz isn’t necessary
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | FFS | FFS |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.

## Slide 7: WF 1
Take Option 2 and Alt 1-2from [3] as package agreements
  -8dBm/200MHz requirements is not needed and will be removed
  NS_202 includes harmonic requirements (Requirement 4) and +1 dBm/200 MHz (Requirement 2)
  Take A-MPR values proposed in WF3
    +1dBm/200MHz for n257 & 7dBm/1GHz for n259 are introduced into NS_200, respectively, according to the previous agreements.
  Newly introduced NS is mandatory for UE brought into use at least after the changeover date
    Whether NS_201 can be repurposed to signal the -5dBm/200MHz requirement is FFS
    Whether mandatory or not for UE brought into use before the changeover date is FFS
      FFS how to avoid mandating UEs to meet NS_204 before it is required in regulations, e.g. until 2024 in EU and 2027 in JP/US.
    FFS if mandatory status of NS is tied to release version
NOTE: This WF is applicable to WRC-19 requirements.
Notes: Qualcomm: Add note about tying NS mandatory status to release version to accommodate testing and verification considerations.
Docomo: Move a sentence from one column to another(Brown one), which is editorial change
Apple: we should consider the option of repurposing NS_201 to signal the -5 dBm/200 MHz requirement for UEs compliant with the WRC-19 regulation

## Slide 8: WF 2
For handling of NS_201, whether repurposing NS_201 is FFS
  If repurpose NS_201, the following should be discussed
    Whether modified MPR for NS_201 is needed or not
    The descriptive Text in CR [5] should be same with that in CR [6] (It depends on whether alt 1-2 will be taken)
  If not repurpose NS_201, the following should be discussed
    Whether or not NS_201 is obsolete
Notes: Qualcomm: In general, we do not think repurposing NS_201 for a new requirement is a good idea, due to possible existence of fielded UEs. We are ok to leave it ‘orphaned’ but would prefer making obsolete to reduce UE testing. We can revisit this avenue if we define more than 8 NS values in each band and it is critical to repurpose disused NS.
DOCOMO(Green): Change the structure in this slide which is editorial change.

## Slide 9: WF3: A-MPR values
NOTE: see R4-2006788 [4] for definitions of offset frequency and edge allocation
Band | Requirement | A-MPR for PC1 | A-MPR for PC2 | A-MPR for PC3 | A-MPR for PC4
n258 | Protected range: 23.6 - 24.0 GHz Limit: +1 dBm/200 MHz | 3.0 if Offset frequency < BWchannel, 0.0 otherwise | 0 | 0 | 0
n257 |  | 0 (absorb as general requirement) | 0 (absorb as general requirement) | 0 (absorb as general requirement) | 0 (absorb as general requirement)
n258 | Protected range: 23.6 - 24.0 GHz Limit: -5 dBm/200 MHz | 7.0 if Offset frequency < BWchannel, 6.0 otherwise | 1.0 if Offset frequency < BWchannel, 0.0 otherwise | 1.0 if Offset frequency < BWchannel, 0.0 otherwise | 1.0 if Offset frequency < BWchannel, 0.0 otherwise
n257 |  |  |  |  | 
n260 | Protected range: 36.0 to 37.0 GHz Limit: +7 dBm/1000 MHz and -13 dBm/1 MHz | >0 for low edge allocations (see below) | >0 for low edge allocations (see below) | >0 for low edge allocations (see below) | >0 for low edge allocations (see below)
n259 |  | 0 (absorb as general requirement) | 0 (absorb as general requirement) | 0 (absorb as general requirement) | 0 (absorb as general requirement)
Notes: Apple: we suggest capturing the table of A-MPR values from the Moderator summary for clarity, since the CR in R4-2006788 included many other aspects, such as detailed NS design, which is still under discussion at the moment
Qualcomm: We recommend capturing contents of the CR stripped of details that are still under discussion, rather than a summary table above. There is risk in this kind of transposition that some details are lost, as is evident above. We prefer all details move together. It is ok to leave all the details out if that is preferred by RAN4

## Slide 10: WF3a – AMPR values
6.2.3.4 A-MPR for emissions requirements in table below
6.2.3.4.1 power class 1
For intra-band UL CA the following rule for AMPR (dB) applies:
AMPR = AMPRCC
Where:
AMPRCC is 3.0 if Offset frequency < BWchannel, 0.0 otherwise
Offset frequency is defined as the frequency from 24.0 GHz to the lower edge of the channel
6.2.3.4.2 power class 2
For power class 2, AMPR specified in subclause 6.2.3.4.3 applies
6.2.3.4.3 power class 3
For power class 3, AMPR shall be 0 dB.
6.2.3.4.4 power class 4
For power class 4, AMPR specified in subclause 6.2.3.4.3 applies.
Frequency band (GHz) | Spectrum emission limit (dBm) | Measurement bandwidth
23.6 £ f £ 24.0 | +1 | 200 MHz

## Slide 11: WF3b – AMPR values
Frequency band (GHz) | Spectrum emission limit (dBm) | Measurement bandwidth
23.6 £ f £ 24.0 | -5 | 200 MHz
6.2.3.5 A-MPR for emissions requirements in table below
6.2.3.5.1 power class 1
For intra-band UL CA the following rule for AMPR (dB) applies:
AMPR = AMPRCC
Where:
AMPRCC is 7.0 if Offset frequency < BWchannel, 6.0 otherwise
Offset frequency is defined as the frequency from 24.0 GHz to the lower edge of the channel
6.2.3.5.2 power class 2
For power class 2, AMPR specified in subclause 6.2.3.5.3 applies
6.2.3.5.3 power class 3
For intra-band UL CA the following rule for AMPR (dB) applies:
AMPR = AMPRCC
Where:
AMPRCC is 1.0 if Offset frequency < BWchannel, 0.0 otherwise
Offset frequency is defined as the frequency from 24.0 GHz to the lower edge of the channel
6.2.3.5.4 power class 4
For power class 4, AMPR specified in subclause 6.2.3.5.3 applies.

## Slide 12: WF3c – AMPR values
6.2.3.6 A-MPR for emissions requirements in table below
6.2.3.6.1 power class 1
For power class 1, AMPR shall be 0.0 dB unless the allocation meets the following conditions to qualify as a low-edge allocation:
RBstart < BWchannel/10 MHz
RBstart  LCRB/2
Offset frequency < 10% of BWchannel
Where:
Offset frequency is defined as the frequency from 37.0 GHz to the lower channel edge
The AMPR (dB) for low-edge allocations is shown on right.
PC1 | BWchan (MHz) |  |  | 
 | 50 | 100 | 200 | 400
A-MPR(dB) | 16.0 | 14.0 | 7.0 | 6.0
6.2.3.6.2 power class 2
For power class 2, AMPR specified in subclause 6.2.3.6.3 applies
6.2.3.6.3 power class 3
For power class 3, AMPR shall be 0.0 dB unless the allocation meets the following conditions to qualify as a low-edge allocation:
RBstart < BWchannel/10 MHz
RBstart  LCRB/2
Offset frequency < 10% of BWchannel
Where:
Offset frequency is defined as the frequency from 37.0 GHz to the lower channel edge
The AMPR (dB) for low-edge allocations is shown on right.
PC3 | BWchan (MHz) |  |  | 
 | 50 | 100 | 200 | 400
A-MPR(dB) | 12.0 | 10.0 | 3.0 | 2.0
6.2.3.6.4 power class 4
For power class 4, AMPR specified in subclause 6.2.3.6.3 applies.
Frequency band (GHz) | Spectrum emission limit (dBm) | Measurement bandwidth
36.0 £ f £ 37.0 | +7 | 1000 MHz
 | -13 | 1 MHz

## Slide 13: References
[1] R4-2000220, “Necessity of signaling supported NS values”, NTT DOCOMO, INC.
[2] R4-2003241, “More on necessity of signaling supported NS values”, NTT DOCOMO, INC., KDDI Corporation, SoftBank Corp.,
[3] R4-2005738, “WF on WRC-19 outcome and impact on RAN4 specifications”, NTT DOCOMO, INC.
[4] R4-2006788, “dCR to 38.101-2: Introduction of NS flags and A-MPR from WRC19 Resolutions”, Qualcomm Incorporated
[5] R4-2008163, “CR for modified MPR on NS_201”, Huawei, HiSilicon
[6] R4-2007038, “Introduction of the Annex modifiedMPR-Behaviour into the NR SA specification”, Ericsson