## Slide 1: WF on MPR/A-MPR requirements for S-SSB transmission
Qualcomm
3GPP TSG-RAN WG4 NR #95e
25th May - 5th June 2020
R4-2008441

## Slide 2: Open Issues
Issue 1-3-1: MPR for S-SSB transmission
Proposals
  Option 1: Define the allowed MPR for NR V2X S-SSB in LGE paper (R4-2006746). The format and level are almost same as Huawei proposal.
  Option 2: Define the allowed MPR for NR V2X S-SSB in QC paper (R4-2006820).
  Option 3: compromise MPR based on two options
Issue 1-3-2: A-MPR for S-SSB transmission
Proposals
  Option 1: A-MPR for update ETSI regulation will be defined with new_NS in TS38.101-1 when ETSI releases the updated regulation requirement.
  Option 2: A-MPR for update ETSI regulation will be defined with existing NS_33 to comply updated A-SE in TS38.101-1 when ETSI releases the updated regulation requirement.

## Slide 3: WF on MPR/A-MPR requirements for S-SSB transmission
The following tables are suggested as a WF on MPR/A-MPR requirements for S-SSB transmission:
MPR for S-SSB transmission
Table 1- S-SSB MPR requirements SCS= 15 kHz, 30 kHz, 60 kHz
  Note1: Inner and outer allocations based on sect. 6.2.2 TS38.101-1
Channel | MPR (dB) | 
 | Outer RB allocations1 | Inner RB allocations1
S-SSB | ≤ [6.0] | ≤ [2.5]
NOTE 1: Inner and Outer RB allocations are defined in section 6.2.2 TS38.101-1 |  | 

## Slide 4: WF on MPR/A-MPR requirements for S-SSB transmission
A-MPR for NS_33 S-SSB transmission
Carrier Frequency (MHz) | RBStart | A-MPRBase (dB) | AMPRStep (dB)
5860 | 0 to 1 | ≤ 25 | 0
 | 2 to 4 | ≤ 12 | 0.20
 | 5 to 7 | ≤ 10.5 | 0.30
 | 8 to 10 | ≤ 8 | 0.35
 | 11 to 13 | ≤ 7 | 0.4
5870, 5880, 5890, 5900,5910, 5920 | 0 to 1 | ≤ 5.5 | 0.4
 | 2 to 4 | ≤ 4.5 | 
 | 5 to 6 | ≤ 3.0 | 
 | 7 | ≤ 2.5 | 
 | 8 to 9 | ≤ 3.0 | 
 | 10 to 11 | ≤ 4.5 | 
 | 12 to 13 | ≤ 6.0 | 
SCS=30 kHz
Carrier Frequency (MHz) | RBStart | A-MPRBase (dB) | AMPRStep (dB)
5860 | 0 to 1 | ≤ 25 | 0
 | 2 to 3 | ≤ 17 | 0.1
 | 4 to 7 | ≤ 14 | 0.15
 | 8 to 10 | ≤ 8.5 | 0.20
 | 11 to 15 | ≤ 7.5 | 0.25
 | 16 to 20 | ≤ 4.5 | 0.35
 | 21 to 30 | ≤ 3.0 | 0.45
 | 31 to 35 | ≤ 3.5 | 0.55
 | 36 to 40 | ≤ 7.5 | 0.6
5870, 5880, 5890, 5900, 5910, 5920 | 0 to 1 | ≤ 6 | 0.7
 | 2 to 7 | ≤ 5.0 | 
 | 8 to 11 | ≤ 4.0 | 
 | 12 to 13 | ≤ 2.5 | 
 | 14 to 25 | 0 | 
 | 26 to 29 | ≤ 2.0 | 
 | 30 to 34 | ≤ 4.0 | 
 | 35 to 36 | ≤ 5.0 | 
 | 37 to 40 | ≤ 6.0 | 
SCS=15 kHz
Carrier Frequency (MHz) | RBStart | A-MPRBase (dB) | AMPRStep (dB)
5860 | 0 | ≤ 25 | 0
5870, 5880, 5890, 5900,5910, 5920 | 0 | ≤ 5.5 | 0.85
SCS = 60 kHz
Note 1:
RB_start=0 to 18 AMPRStep= (RB_start)*0.3/18
RB_start=19 to 40 AMPRStep= 0.3+(RB_start-18)*0.3/23
Note 2:
RB_start=0 to 6 AMPRStep= (RB_start)*0.25/6
RB_start=7 to 13 AMPRStep= 0.25+(RB_start-6)*0.15/7

## Slide 5: WF on MPR/A-MPR requirements for S-SSB transmission
A-MPR for NS_NEW S-SSB transmission
Carrier Frequency (MHz) | RBStart | A-MPR (dB)
5870, 5880, 5890, 5900, 5910, 5920 | 0 to 1 | ≤ 5.5
 | 2 to 4 | ≤ 4.5
 | 5 to 6 | ≤ 3.0
 | 7 | ≤ 2.5
 | 8 to 9 | ≤ 3.0
 | 10 to 11 | ≤ 4.5
 | 12 to 13 | ≤ 6.0
SCS=30 kHz
Carrier Frequency (MHz) | RBStart | A-MPR (dB)
5860, 5870, 5880, 5890, 5900, 5910, 5920 | 0 to 1 | ≤ 6
 | 2 to 7 | ≤ 5.0
 | 8 to 11 | ≤ 4.0
 | 12 to 13 | ≤ 2.5
 | 14 to 25 | 0
 | 26 to 29 | ≤ 2.0
 | 30 to 34 | ≤ 4.0
 | 35 to 36 | ≤ 5.0
 | 37 to 40 | ≤ 6.0
SCS=15 kHz
Carrier Frequency (MHz) | RBStart | A-MPR(dB)
5860, 5870, 5880, 5900, 5890, 5910, 5920 | 0 | ≤ 5.5
SCS = 60 kHz

## Slide 6: WF on MPR/A-MPR requirements for S-SSB transmission
A-MPR for NS_52 S-SSB transmission
Carrier Frequency (MHz) | RBStart * 12*SCS [MHz] | A-MPR (dB)
58851 | ≤ 7 | ≤ 16
 | > 7and ≤ 12 | ≤ 10.5
 | > 12 and ≤ 19 | ≤ 4.0
 | > 19 and ≤ 25 | ≤ 10.5
 | > 25 | ≤ 16
NOTE 1: Applies only when NS_52 is signalled |  | 

## Slide 7: WF on MPR/A-MPR requirements for S-SSB transmission
MPR table format as RB start/ RB_stop
NS_33 and NS_NEW format as RB start/ RB_stop
NS_52 format based on frequency range =RB_start*12*SCS
Can further discuss changing A-MPR table format to match that of NS_52