## Slide 1: WF on MR-DC RRM requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #95e
E-meeting, May 25th – June 5th, 2020
R4-2008602
Document for: Approval

## Slide 2: Background
During the RAN4#95e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Agreements during are captured in this WF.
Agreements from previsous meetings are captured in:
  Approved WFs during the meeting
  Draft Big CRs for 36.133 and 38.133
Summary of the round 1 discussion during RAN4#95e meeting is captured in R4-2008501.
Round 2 discussions is captured in R4-2009024
Agreements reached are captured in this WF
  Tentative agreements for conclusion are also listed in this WF.
Additional a number of open issues for further discussion were listed. Also those are listed in this WF.

## Slide 3: Agreements after round 1
Total number of NR inter-frequency EMR carriers ≤7 carriers
Total number of LTE inter-RAT EMR carriers ≤7 carriers
Following pages includes a number of tentative agreements. Companies are encouraged to comment and compromise in the email discussion as well as here.

## Slide 4: Tentative Agreements after round 1
UE requirements concerning number of EMR carriers (1-3 and 1-9):
  RAN4 confirm, that same principle assumptions which currently applies concerning UE measurement capability would also apply to UE measurement capability of carriers configured for EMR.
  RAN4 to specify a total number of EMR carriers the UE shall be able to measure.
  There is no need to distinguish overlapping and non-overlapping EMR carriers when considering the total number of EMR carriers.
  RAN4 will discuss and define a number of non-overlapping NR inter-frequency and/or LTE inter-RAT EMR carriers the UE at least need to be able to measure.
  Considering the total number of overlapping EMR carriers the UE at least shall be able to measure:
    The UE shall at least be able to measure:
      Overlapping LTE inter-RAT EMR carriers ≤7 LTE carriers
      Overlapping NR inter-frequency EMR carriers ≤7 NR carriers

## Slide 5: Tentative Agreements after round 1
UE requirements concerning number of EMR carriers (1-3 and 1-9):
  Number of non-overlapping NR inter-frequency carriers = 7 NR – number of overlapping NR EMR carriers
  Number of non-overlapping LTE inter-RAT carriers = [1, 2] carrier(s)

## Slide 6: Tentative Agreements after round 1
UE requirements related to EMR and beam-level measurement capability (1-4):
  UE is allowed additional measurement time for Index reading in Idle and Inactive mode if the UE has been requested to report EMR with beam Index
  Define UE measurement capability to support beam-level measurements for EMR on inter-frequency NR carriers.
Note: UE requirements related to EMR and beam-level measurement capability may be a UE capability

## Slide 7: Tentative Agreements after round 1
Detected cell conditions details (1-6):
  RAN4 include into the cell detected state condition upon transition to idle/inactive mode that the detected cell status is only applicable on SSB level, i.e. for one cell, UE can consider the SSBs detected in connected mode as also detected when entering into idle mode
  Adopt option 1 and add a condition similar to the condition used in LTE: ‘In the absence or expiration of T331, it is up to UE implementation to apply the requirements on the detected cell status in this subclause’.

## Slide 8: Tentative Agreements after round 1
UE measurement requirements for EMR when T331 has expired (1-7):
  RAN4 will not define UE measurement requirements for EMR when T331 has expired

## Slide 9: Tentative Agreements after round 1
UE requirements related to EMR measurements at cell change (1-8):
  RAN4 will not define requirements at cell change

## Slide 10: Tentative Agreements after round 1
Capturing the UE capability (2-2):
  Capture the UE capability in the requirements. Wording can be discussed further

## Slide 11: Tentative Agreements after round 1
Number of NR Inter-RAT EMR carriers to measure (2-3):
  The number of NR Inter-RAT EMR carriers to measure (total) is 8

## Slide 12: Tentative Agreements after round 1
Cell detected status when entering idle mode (2-4):
  Follow agreement for NR inter-frequency as discussed in Sub-topic 1-6 as closely as possible

## Slide 13: Tentative Agreements after round 1
Beam level measurements for NR Inter-RAT EMR (2-6):
  Define UE measurement capability to support beam-level measurements for EMR on inter-frequency NR carriers
  Beam level measurements for NR Inter-RAT EMR follow agreements for UE requirements related to inter-frequency beam level EMR reporting
  Beam level measurements for NR Inter-RAT EMR follow agreements for UE requirements related to inter-frequency beam level EMR reporting
Note: UE requirements related to EMR and beam-level measurement capability may be a UE capability

## Slide 14: Way Forward
The following pages includes a collection of open issues
These are for discussion in the comming meeting(s)
These are issues left without agreement after 2nd round discussion in the RAN4#95e meeting
Companies are encouraged to bring discussion papers and views at least on those topics for the coming meeting to progress the work.

## Slide 15: Way Forward
Will list any aspects left open for further discussion (38.133):
s-NonIntraSearch thresholds and EMR carriers
Conditions for ‘actively measured’
UE requirements concerning number of EMR carriers
UE requirements related to EMR and beam-level measurement capability
UE measurement requirements for carriers configured for EMR
Detected cell conditions details
UE measurement requirements for EMR when T331 has expired
UE requirements related to EMR measurements at cell change

## Slide 16: Way Forward
Will list any aspects left open for further discussion (36.133):
Scope of Requirements Discussion
Capturing the UE capability
Number of NR Inter-RAT EMR carriers to measure
Cell detected status when entering idle mode (follow discussion for 38.133)
Measurement requirements for overlapping NR inter-RAT EMR carrier
Beam level measurements for NR Inter-RAT EMR
Measurement requirements for non-overlapping NR Inter-RAT EMR carrier