## Slide 1: Way Forward on SCell Dormancy
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25 – June 5, 2020
R4-2008607
Document for: Approval

## Slide 2: Background
At RAN4#94e, agreements on SCell dormancy were captured in R4-2002238 “WF on UE RRM requirements for dormancy SCell”
At RAN4#94e-Bis, agreements on SCell dormancy were captured in R4-2005329 “Way Forward on SCell Dormancy”

## Slide 3: Background
At RAN4#95e, the following topics were discussed:
Sub-topic 2-1: Switching of single SCell between dormancy and non-dormancy, triggering inside active time
  Issue 2-1-1: Switching delay non-dormancy to dormancy, general case w.r.t. parameter change
  Issue 2-1-2: Switching delay non-dormancy to dormancy, optimized w.r.t. parameter change
  Issue 2-1-3: Switching delay dormancy to non-dormancy, general case w.r.t. parameter change
  Issue 2-1-4: Switching delay dormancy to non-dormancy, optimized w.r.t. parameter change
  Issue 2-1-5: Interruption at switching between dormancy and non-dormancy
Sub-topic 2-2: Switching of single SCell between dormancy and non-dormancy, triggering outside active time
  Issue 2-2-1: Switching delay between dormancy and non-dormancy
  Issue 2-2-2: Interruption at switching between dormancy and non-dormancy
Sub-topic 2-4: CSI and RRM measurements during dormancy
  Issue 2-4-1: Measurement requirements
  Issue 2-4-2: Interruptions

## Slide 4: 2-1-1: Switching delay non-dormancy to dormancy, general case w.r.t. parameter change (1/2) [Inside active time]
Agreement:
For general case w.r.t. parameter change, and conditioned on that DCI is received within the first 3 OFDM symbols, switching between non-dormancy and dormancy follows the Rel-15 BWP switching time in Table 8.6.2-1.

## Slide 5: 2-1-1: Switching delay non-dormancy to dormancy, general case w.r.t. parameter change (2/2) [Inside active time]
Agreement:
  For DCI-based triggering with DCI received in any of the first X OFDM symbols of a slot, and for timer-based triggering, the switching delay for transition from non-dormancy to dormancy is given by Table 8.6.2-1.
  For DCI-based triggering with DCI received after the first X OFDM symbols of a slot, if applicable, the switching delay for transition from non-dormancy to dormancy is given by Table 8.6.2-1 plus Z additional slot(s).
  For value of X:
    Option 1a: X = 3 symbols
    Option 1b: X = 7 symbols
  For value of Z:
    Option 2a: Z = 1 slot in numerology for the spCell in which the triggering DCI was received
    Option 2b: Z = 1 slot in the numerology for the SCell for which the transition is triggered
  In case SCS differs between spCell and SCell, the switching delay, except for Z slot(s), associated with the smaller SCS applies.

## Slide 6: 2-1-2: Switching delay non-dormancy to dormancy, optimized w.r.t. parameter change [Inside active time]
For further discussion:
Option 1: Only introduce generic requirements. Optimizations can be introduced as future enhancements.
Option 2: Rel-15 Type-1 BWP switch delay apply for dormancy switch if only parameters for PDCCH monitoring and CSI-RS reporting differ between regular BWP and dormant BWP.

## Slide 7: 2-1-3: Switching delay dormancy to non-dormancy, general case w.r.t. parameter change [Inside active time]
Agreement:
The dormancy switching delay for switching between dormancy and non-dormancy is same as for switching between non-dormancy and dormancy. (Conclusion for 2-1-1 applies here too)

## Slide 8: 2-1-4: Switching delay dormancy to non-dormancy, optimized w.r.t. parameter change [Inside active time]
Agreement:
The dormancy switching delay for switching between dormancy and non-dormancy is same as for switching between non-dormancy and dormancy. (Conclusion for 2-1-2 applies here too)

## Slide 9: 2-1-5: Interruption at switching between dormancy and non-dormancy [Inside active time]
For further discussion:
Option 1: Rel-15 BWP switch interruption requirements apply for dormancy switch triggered within DRX active time. Interruption additionally allowed for toggling RF on/off.
Option 2: Interruption length as in Table 8.2.2.2.5-1 applies. The interruption time window is confined within the BWP switching delay for transition between dormancy and non-dormancy. If UE is capable of per-FR gap, UE is allowed to cause interruption of up to X slot to other active serving cells in the same frequency range. If UE is not capable of per-FR gap, UE is allowed to cause interruption of up to X slot to other active serving cells. Interruptions are allowed regardless of which parameters change between dormancy and non-dormancy.
Option 3: Follow normal BWP change interruption requirements, i.e., no interruption when neither of locationAndBandwidth, nrofSRS-Ports, maxMIMO-Layers, or SCS, changes.

## Slide 10: 2-2-1: Switching delay between dormancy and non-dormancy [Outside active time]
For further discussion:
Option 1: Same set of switch delay requirements shall apply for triggering outside active time (DCI 2_6) as for triggering inside active time (e.g. DCI 0_1).
Option 2: BWP switch delay for scheduled and non-scheduled DCI dormancy switch delay would be covered by the DCI BWP switch delay requirement. WUS based dormancy BWP switch does not lead to visible switch delay provided the WUS is received early enough before On-duration.
Option 3: RAN4 to further wait for RAN1 conclusion to see if visible delay and interruption requirements are needed.

## Slide 11: 2-2-2: Interruption at switching between dormancy and non-dormancy [Outside active time]
For further discussion:
Option 1: Same interruption requirement apply for triggering outside as for inside active time.
Option 2: RAN4 to wait for RAN1 conclusions before defining interruption requirements for dormancy switch triggered outside DRX active time.

## Slide 12: 2-4-1: Measurement requirements for CSI and RRM measurements during dormancy
Agreement:
UE measurement requirements are same for dormant as for non-dormant SCell.

## Slide 13: 2-4-2: Interruptions for CSI and RRM measurements during dormancy
For further discussion:
Option 1: The legacy principle of LTE can be reused and total interruption requirements for CSI and RRM measurement during SCell dormancy shall not exceed a particular percentage value.
Option 2: For Interruptions due to SSB-based measurements and CSI-RS reception,
  Interruptions are allowed with up to X% probability of missed ACK/NACK with the following conditions
    The UE is only allowed to cause interruptions immediately before and after an SMTC. Each interruption shall not exceed requirement in Table 8.2.2.2.2-1 if victim cells are not in the same band as the aggressor SCell. Each interruption shall not exceed requirement in Table 8.2.2.2.2-2 if victim cells is in the same band as the aggressor SCell.
  Interruptions are allowed with up to Y% probability of missed ACK/NACK with the following conditions
    The UE is only allowed to cause interruptions immediately before and after an CSI-RS OFDM symbol. Each interruption shall not exceed requirement in Table 8.2.2.2.2-1.

## Slide 14: For RAN4#96e
Interested companies are encouraged to provide further analyses on open issues for:
2-1-1: Switching delay non-dormancy to dormancy, general case w.r.t. parameter change
  Value of X. Numerology of Z.
2-1-2: Switching delay non-dormancy to dormancy, optimized w.r.t. parameter change
  Whether to have separate requirements for certain parameter changes.
2-1-5: Interruption at switching between dormancy and non-dormancy
  Whether toggling RF on/off shall be allowed. Whether SCS change results in cross-FR interruption.
2-2-1: Switching delay between dormancy and non-dormancy
2-2-2: Interruption at switching between dormancy and non-dormancy
2-4-2: Interruptions for CSI and RRM measurements during dormancy
  Whether to have ACK/NACK rate, or ACK/NACK rate plus interruption window.