## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT
3GPP TSG-RAN WG4 Meeting #95e R4-2008612
Electronic Meeting, 25th May – 5th June, 2020

## Slide 2: WF on RRM measurement relaxation
scaling factor of measurement interval
  Option 1: The same value (Huawei, vivo, CATT, Qualcomm, Apple, ZTE, CMCC, Nokia)
    2 times (ZTE, Nokia)
    4 times (Huawei, vivo, CATT, Qualcomm, Apple, CMCC)
  Option 2: Different value (Ericsson)
    4 for low mobility scenario and 2 for not-at cell edge scenario (Ericsson)
  The measurement relaxation method for higher priority or equal/lower priority applies to inter-RAT measurement with higher priority or equal/lower priority.
  When network configures the parameters of both low mobility and not-at-cell-edge criteria, if network indicates option b, FFS the relaxation method corresponding to scenario #3 can be applied when both relaxation criteria have been fulfilled

## Slide 3: WF on RRM measurement relaxation
When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, if criteria of low mobility and not in cell edge are both fulfilled,
  UE can stop both equal/low priority and high priority inter-freq/inter-RAT measurements
    1 hour time interval applies to the measurement relaxation since last measurement for cell reselection for higher priority carriers
  When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ and only criteria of low mobility is configured, if the low mobility criteria is fulfilled,
    UE can stop equal/low priority measurements
    FFS on the UE measures higher priority inter-frequency/inter-RAT layers.

## Slide 4: WF on minimum requirement at transition period
    When switching from scenario #1 or #2 to scenario #3, the UE shall fulfil the requirements corresponding to scenario #1 or #2 for N DRX cycles and thereafter switch to requirements corresponding to scenario #3
    When switching from scenario #3 to scenario #1 or #2, the UE shall fulfil the requirements corresponding to scenario #1 or #2 upon fulfilling the switching criteria.
    When switching from normal mode to scenario #1/#2/#3, the UE shall fulfil the requirements corresponding to normal mode for N DRX cycles and thereafter switch to requirements corresponding to scenario #1/#2/#3
    When switching from scenario #1/#2/#3 to normal mode, the UE shall fulfil the requirements corresponding to normal mode upon fulfilling the switching criteria.

## Slide 5: WF on RRM measurement relaxation
The evaluation rate for measurement relaxation mode triggering shall be the same as current serving cell evaluation rate defined in 38.133
RAN4 not specify intra/inter-frequency requirement when the threshold configured for not-at-cell-edge condition is higher than that for cell center condition of “SnonIntraSearchP” or “SnonIntraSearchQ”.
  This rule also applies in “SIntraSearchP” or “SIntraSearchQ”.
Measurements on EMR carriers should not be relaxed if T331 is running
It is up to RAN2’s decision on whether to introduce carrier specific threshold for inter-frequency measurement relaxation.