## Slide 1: 3GPP TSG-RAN WG4 Meeting #95-e Electronic Meeting, 25 May – 5 June, 2020
Intel
WF on requirements for NR Positioning PRS-RSRP, SSB and CSI-RS RSRP/RSRQ measurements
R4-2008666

## Slide 2: Report mapping
Differential PRS-RSRP reporting range for FDM-ed resources
  Option 1. The reporting range for differential reporting for PRS RSRP measurements on FDM-ed PRS resources is [-27 dB; 27 dB] or smaller
  Option 2. The reporting range of ±30 dB for PRS-RSRP differential report can be applicable in both TDM and FDM case.

## Slide 3: Definition of intra/inter-frequency measurement
Do NOT define intra/inter-frequency definition for PRS-RSRP
  Note: Classification of accuracy requirements is FFS (e.g. whether to define different accuracy for measurements on different frequencies)

## Slide 4: Scenarios of PRS RSRP measurement requirements
RAN4 requirements are to be defined only for the case where PRS is measured with configured measurement gap

## Slide 5: Measurement period for PRS RSRP
Given the PRS-RSRP needed in different NR positioning methods, the principle for defining PRS- RSRP measurement period can be
  when configured with UE Rx-Tx, PRS-RSRP measurement period can be same as that of UE Rx-Tx measurement
  when configured with RSTD, PRS-RSRP measurement period can be same as that of RSTD measurement
  FFS: when not configured with either UE Rx-Tx or RSTD.

## Slide 6: Measurement capability
Option 1: RAN4 needs not to define measurement capability in terms of number of PRS layers, TRPs, resource sets and resources that UE shall be able to measure
Option 2: RAN4 needs to define the numbers (of TRPs, cells, PRSs, etc.) for which the requirements apply in 38.133.
  FFS: Whether these numbers are the same as or smaller than those in the signalling

## Slide 7: Reporting criteria
If PRS-RSRP measurements are not configured together with other reporting (e.g.RSTD in DL TDoA, UE Rx-Tx time difference in multi-RTT), the separated measurement reporting criteria for them is needed as below
  Ecat=1

## Slide 8: Side condition
For DL-OTDOA and Multi-RTT positioning methods, the side condition of PRS RSRP should follow these of RSTD and UE Rx-Tx time difference measurement respectively.
For DL-AoD, the side condition of PRS RSRP can be specified
  Option 1: for both serving cell/TRP and neighbor cell/TRPs.
    For serving cell:
      Option 1-1: -6 dB
      Option 1-2. -3 dB
  Option 2 :for neighbor cell/TRPs ONLY.
  Option 3: For the reference cell/TRPs and neighbour cell/TRPs
    Same as that for the reference cell in PRS-RSTD

## Slide 9: Measurement accuracy requirements for PRS RSRP
Number of samples for PRS RSRP measurement accuracy:
  Option 1: 1 sample includes resource repetitions within the PRS occasion
  Option 2: depends on the required number of comb realizations (NPRS,req)
    FFS: Whether RSTD accuracy is agnostic to comb
      Companies are encouraged to study the impact of number of symbols within a slot
Types of requirements
  Option 1: Define absolute accuracy requirements ONLY
  Option 2: Define relative accuracy requirements ONLY
  Option 3: Define both absolute and relative accuracy requirements