## Slide 1: WF on IAB-MT supported channel bandwidth
Samsung,…
3GPP TSG-RAN WG4 Meeting #95-e R4-2008772
Electronic Meeting, 25th May– 5th June, 2020

## Slide 2: Background
RAN4 agreed in [1] that : “IAB-MT declares all the supported channel bandwidths rather than having a mandatory set as current UEs. The parent/donor should be aware of the channel bandwidths supported by the MT.” And RAN2 is working on the signalling detail.
This WF is to analyse the initial access procedure impact on IAB-MT supported channel bandwidth based on the legacy agreement for UE regarding “supported bandwidth for initial BWP” in [2].

## Slide 3: Agreement on IAB-MT channel bandwidth dependency on SIB1 channel bandwidth and initial BWP-bandwidth in initial access
According to 1st round discussion summary in [3] below agreement in green is suggested to included in TR:
  RAN4 agreed that “IAB-MT can access the cell if IAB-MT supports a channel bandwidth which is equal to or narrower than the channel bandwidth in SIB1 and is equal to or wider than the initial BWP-bandwidth.”
  BWP-bandwidth can be configured with any number of RBs equal to or narrower than RB size of the supported channel bandwidths.
  Although the core requirement is applied to any RB configuration, it is noted that only the set of supported channel bandwidths are included in conformance tests due to the test coverage limitation.

## Slide 4: On IAB-MT channel bandwidth and COEESET#0[information]
UE uses CORESET#0 bandwidth to acquire the PDCCH information and blind detect for SIB1. UE will keep the downlink bandwidth of CORSET#0 until after reception of RRCSetup/RRCResume/RRCReestablishment, which means UE will use CORSET#0 bandwidth to receive msg2 and msg4 for random access and RRC connection setup. UE cannot execute random access procedure if it cannot support the CORSET#0 bandwidth.
However, CORESET#0 bandwidth is not verified for UE since all UEs are expected to support all allowed CORESET#0 bandwidths as defined in TS38.213, which may not be the case for IAB-MT.
According to TS 38.213 the CORESET#0 channel bandwidth for operating bands to be supported by IAB is summarized as table below
For FR1, for existing requested operating bands on IAB, the CORSET#0 BW is in the lower end of CHBW(s) of the operating band or even smaller than the minimum CHBW in the CHBW of n79.
For FR2, the 50MHz and 100MHz should be mandatory channel bandwidth to be supported by IAB-MT to ensure initial access procedure.
Operating band | CORESET #0 BW(MHz)
n41 | 5, 10, 20
n77, n78 | 5,10, 20
n79 | 10, 20
n257, n258, n260, n261 | 50, 100

## Slide 5: WF for CHBW supported by IAB-MT [To be agreed]
For operating band in FR1 the channel bandwidth to be supported by IAB-MT should be within the CHBW addressed in Table 5.3.5-1 of the TS38.104.
For operating band in FR2 the channel bandwidth to be supported by IAB-MT should be within the CHBW addressed in Table 5.3.5-2 of the TS38.104.
For FR2 operating band, 50MHz and 100MHz should be mandatory supported by IAB-MT to ensure initial access.

## Slide 6: Reference
[1] R4-1916165, LS on definition of IAB-MT channel bandwidth
[2] R4-1910522, LS reply on supported BW for initial BWP
[3] R4-2008696 Email discussion summary for [95e][307] NR_IAB_Featurelist
[4] R4-2006798 Clarification on IAB-MT supported channel bandwdith