## Slide 1: Way Forward on PMI Reporting Test Cases with Rel-16 Type II Codebook
Qualcomm, Ericsson
3GPP TSG-RAN4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020
Agenda item: 6.11.3.3
R4-2008816
Document for: Approval

## Slide 2: Enhanced Type II Test Setup
Test setup:
  Option 1: Only use SU-MIMO test setup, i.e., one tested UE
  Option 2: MU-MIMO based test setup, i.e., one tested UE + one co-scheduled UE (generated by TE)
The baseline receiver assumption is UE without interference cancellation capability with/without co-scheduled UE.
Under the baseline UE receiver assumption, the PMI calculation processing will not change with and without co-scheduled UE.
TE vendors are encouraged to provide feedback for the test feasibility of MU-MIMO test setup.
Proponents for each option need to provide technical analysis for how the test set-up can guarantee UE PMI reporting requirements with enhanced type II codebook for its intended purpose.

## Slide 3: Test Parameters for Option 1 Test Setup - I
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4) as baseline
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  Option 1: R = 1 as baseline
  Option 2: R = 2

## Slide 4: Test Parameters for Option 1 Test Setup - II
Codebook parameter configuration
  Option 1: paramCombination-r16: 6, with L =4, pν =1/2, β=1/2 as baseline
  Other options not precluded
Sub-band Size:
  Option 1:
    4 for FDD with 15kHz SCS, 10MHz CBW
    8 for TDD with 30kHz SCS, 40MHz CBW
  Option 2:
    8 for FDD with 15kHz SCS, 10MHz CBW
    16 for TDD with 30kHz SCS, 40MHz CBW

## Slide 5: Test Parameters for Option 1 Test Setup - III
Beam-Steering Model
  Configure only two beams in beam steering model for Rel-16 Type II test cases.
  FFS how to specify beam steering model into specification.
    Option 1: Same as specified in B.2.3B.4A of TS 36.101
    Option 2: Specify using generic number of beams.

## Slide 6: Test Parameters for Option 1 Test Setup - IV
Channel Model
  TDLA30-5 as baseline
  Other options not precluded
MIMO Correlation
  Option 1: XP High
  Option 2: XP Medium
  Down-select to one option based on simulation results in the next meeting
MCS and Rank
  MCS 20 (64QAM Table), Rank 2 as baseline
  Other options not precluded

## Slide 7: Simulation Assumptions for Option 1 Test Setup
For initial simulations:
  Use the parameters listed in previous slides.
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2008847.

## Slide 8: Test Parameters for Option 2 Test Setup - I
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4) as baseline
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  Option 1: R = 1 as baseline
  Option 2: R = 2

## Slide 9: Test Parameters for Option 2 Test Setup - II
Codebook parameter configuration
  Option 1: paramCombination-r16: 6, with L =4, pν =1/2, β=1/2 as baseline
  Other options not precluded
Sub-band Size:
  Option 1:
    4 for FDD with 15kHz SCS, 10MHz CBW
    8 for TDD with 30kHz SCS, 40MHz CBW
  Option 2:
    8 for FDD with 15kHz SCS, 10MHz CBW
    16 for TDD with 30kHz SCS, 40MHz CBW

## Slide 10: Test Parameters for Option 2 Test Setup - III
Beam-Steering Model
  Configure only two beams in beam steering model for Rel-16 Type II test cases.
  FFS how to specify beam steering model into specification.
    Option 1: Same as specified in B.2.3B.4A of TS 36.101
    Option 2: Specify using generic number of beams.
  FFS if beam steering model needs to be modified to account for co-scheduled UE.

## Slide 11: Test Parameters for Option 2 Test Setup - IV
Channel Model
  TDLA30-5 as baseline
  Other options not precluded
MIMO Correlation
  Option 1: XP High
  Option 2: XP Medium
  Down-select to one option based on simulation results in the next meeting
MCS and Rank
  MCS 20 (64QAM Table), Rank 2 as baseline
  Other options not precluded

## Slide 12: Test Parameters for Option 2 Test Setup - V
Test Metric
  Option 1: Relative Throughput ratio between following PMI for Rel-16 enhanced Type II and Rel-15 Type II codebook.
  Option 2: Relative throughput ratio between following PMI and random PMI.
  Other options not precluded.

## Slide 13: Scheduling Parameters for Option 2 Test Setup
Channel model for co-scheduled UE
  Option 1: Possibility for spatially separated from DUT
  Other options not precluded
Scheduling mode:
  Option 1: Zero-forcing
  Other options not precluded
DCI value for antenna mapping (Table 7.3.1.2.2-2 from 38.212):
  Option 1: DUT = 3 with DMRS seed=0, co-scheduled UE=5 with random DMRS seed (Rank 1, DMRS antenna port mapping 1000 for DUT, 1002 for co-scheduled UE)
  Option 2: DUT = 7 with DMRS seed=0, co-scheduled UE=8 with random DMRS seed, (Rank 2, DMRS antenna port mapping [1000, 1001] for DUT, [1002, 1003] for co-scheduled UE)
  Other options not precluded

## Slide 14: For Information: ZF Precoder Algorithm for Option 2 Test Setup
W = HT*(H*HT + λI)-1, where
  H = [Ha Hb], where
    Ha is the channel estimated for DUT i.e., Ha= WaT reported type II PMI
    Hb is the channel of co-scheduled UE
      FFS whether Hb= WbT (reported PMI), or if Hb is generated channel.
  W = [Wa Wb]
    Wa is the DUT precoder
    Wb is the co-scheduled UE precoder