## Slide 1: WF on BS Antenna parameters for the SI on 6.425-7.125GHz and 10.0-10.5GHz
Huawei, Nokia, [xxxx]
3GPP TSG-RAN WG4 Meeting #95-e
Electronic meeting, 25 May – 5 June 2020
R4-2008926

## Slide 2: Agreements on BS antenna parameters
Parameter | Macro Sub-urban | Macro Urban | Micro Urban
Am (dB) | 30 | 30 | 30
SLAv (dB) | 30 | 30 | 30
LE (dB) | 2 | 2 | 2
j3dB (deg.) | 90 | 90 | 90
q3dB (deg.) | 65 | 90 | 90
GE,max (dBi) | 6.4 | 5.5 | 5.5
(M, N) (Note 1) | (16, 8) | (16, 8) | (8,8)
Horizontal radiating element spacing | 0.5l | 0.5l | 0.5l
Vertical radiating elements spacing | 0.7l | 0.5l | 0.5l
Horizontal coverage range (deg.) | +/- 60 | +/- 60 | +/- 60
Vertical coverage range (deg.) (Note 2) | 90-100 | 90-120 | 90-120
Total Radiated Power for two polarizations(dBm) | 46 dBm | 46 dBm | [ 41 or 37 dBm]
Note 1: M × N means there are M vertical and N horizontal radiating elements. Note 2: Numbers include mechanical downtilt of TBD degrees. |  |  | 

## Slide 3: References
[1] R4-2006110 AAS BS antenna characteristics for frequency ranges 6.425-7.125GHz and 10.0-10.5GHz Nokia, Nokia Shanghai Bell
[2] R4-2006288 Antenna characteristics CATT
[3] R4-2006924 Array antenna model parameters Ericsson
[4] R4-2007309 Antenna characteristics on 6.425-7.025GHz, 7.025-7.125GHz and 10.0-10.5 GHz Huawei, HiSilicon
[5] R4-2007393 Discussion on NR BS antenna parameters ZTE Corporation