## Slide 1: WF on BC based on CSI-RS
Samsung,
R4-2009142
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – Jun 5th 2020
Agenda: 6.14.1.2

## Slide 2
In RAN4 #94Bis-e, most of side conditions for BC based on CSI-RS have been agreed in the approved WF [1] except the following open issues:
  PSD configuration of SSB when P1 CSI-RS QCL info is type D to SSB for CSI-RS based BC
  whether P1 CSI-RS QCL info as ‘none’ can be considered for CSI-RS only BC
In RAN4 #95-e, discussions [2] are focused on above open issues
  Alternative methods proposed in contributions on PSD configuration of SSB are the same as last meeting
    A hybrid approach was proposed during discussion which can simultaneously satisfy several alternatives
  Whether to send LS to RAN1 asking for CSI-RS only beam correspondence necessity and configuration with P1 CSI-RS QCL info as ‘none’
Background

## Slide 3
For BC based on CSI-RS, P1 CSI-RS QCL info is set as Type D to SSB
To address the testability, deployment and test time concerns to following alternatives,
  Alt 2-1-1-1: SSB and CSI-RS are present, but SSB’s PSD is backed-off by X dB from CSI-RS,
  Alt 2-1-1-2: decrease SSB power until UE SSB based SS-SINR measurement reporting is ≤ [-3] dB,
  Alt 2-1-1-3: SSB and CSI-RS are present, but SSB’s PSD is backed-off by [9] dB from Rel-15 SSB’s PSD,
  Alt 2-1-1-4: Decide on PSD difference for CSI-RS and SSB according to an EIRP based calibration procedure,
A hybrid approach can be further discussed shall be adopted for Rel-16 BC based on CSI-RS:
  FFS if PSD of SSB and CSI-RS are configured differently at each angle so that SSB SNR at all AoA are low and CSI-RS SNR are at its target SNR (6dB) at all AoA, i.e.,
    SSB Ês/Iot = (6-Y)dB at UE baseband at each angle
    CSI-RS Ês/Iot = 6dB at UE baseband at each angle
  FFS if PSD of SSB and CSI-RS shall be configured with respect to the radiated requirements reference point
  FFS if this is a reasonable and/or fair test to UEs with different implementations
How to determine the X and Y value
  X and Y is to be determined based on the PSD difference between SSB and CSI-RS in real network typical deployment, e.g. X, Y=[3 to 9] dB
  Choice of X and Y is to be determined based on an evaluation of impact on UE receiver
Way Forward on BC based on CSI-RS

## Slide 4
Does RAN4 need to specify CSI-RS only BC:
  Option 1: Yes, discuss LS
  Option 2: No, not necessary if CSI-RS based BC is specified
Whether to send LS to RAN1 asking for CSI-RS only beam correspondence necessity and configuration with P1 CSI-RS QCL info as ‘none’
  Option 1: Yes, needed
  Option 2: No, not necessary
RAN4 sends an LS to RAN1 to clarify CSI-RS only BC with the following the conditions:
  RAN4 can provide its current thinking in the LS
  Whether RAN1 will reply or not will not affect the RAN4 work on BC based on CSI-RS
Way Forward on CSI-RS only BC

## Slide 5
[1] | R4-2005737 | WF on BC based on CSI-RS | Samsung
[2] | R4-2008312 | Email discussion summary for [95e][122] NR_RF_FR2_req_enh_Part_2 | Moderator(Apple)
References