## Slide 1: WF on NR-U PC3 ACLR and in-band emissions
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #95-e R4-2009165
e-Meeting, May.25th – June.5th 2020

## Slide 2: WF on PC3 ACLR
Two options are discussed for PC3 ACLR
  Option 1: 28dB
  Option 2: 30dB
the following value for PC3 ACLR is agreed:
  ACLR = [28 to 30] dB for PC3 in NR-U

## Slide 3: WF on in-band emissions in NR-U
The following are agreed
  When the PUSCH or PUCCH transmission is shorter than a slot, the in-band emissions measurement interval is reduced by one or more symbols, accordingly.
  Reuse IBE mask from eLAA. It is assumed that TE can derive the location of LO and IQ exceptions based on reported (or assumed) LO location and waveform.
    FFS: RIV=1 and RIV=5 waveforms to be specified for IBE applicability.

## Slide 4: References
[1] R4-2008124 NR-U In-band emissions requirement Qualcomm
[2] R4-2007319 Discussion on NR-U UE ACLR Huawei
[3] R4-2006320 Consideration of in-band emissions for NR-U Huawei